## Slide 1: WF on Inter-RAT Requirements in NR SA and NSA Operations
Ericsson
3GPP TSG-RAN WG4 Meeting AH-1801
San Diego, USA, January 22-26, 2018
R4-1800840

## Slide 2: Inter-RAT Requirements in NR SA
In NR standalone (SA) operation the UE is configured with at least NR PCell.
In this case the inter-RAT requirements shall be defined to support mobility between NR and E-UTRAN in Rel-15:
  The corresponding inter-RAT E-UTRA requirements shall be defined in TS 38.133:
    The requirements shall be defined in RRC IDLE, RRC_INACTIVE and RRC CONNECTED states.
  The corresponding inter-RAT NR requirements shall be defined in TS 36.133:
    The requirements shall be defined in both RRC IDLE and RRC CONNECTED states.

## Slide 3: Inter-RAT GSM Requirements in NSA
In non-standalone (NSA) operation the UE is configured with at least E-UTRA PCell and NR PSCell i.e. EN-DC operation.
In this case the inter-RAT GSM requirements shall be defined to support mobility between E-UTRA FDD and GSM, and between E-UTRA TDD and GSM in Rel-15:
  The corresponding inter-RAT GSM requirements in NSA shall be defined in at least TS 36.133:
    The requirements shall be defined in both RRC IDLE and RRC CONNECTED states.
    Certain requirements (e.g. number of GSM layers to monitor) may also be defined in TS 38.133.

## Slide 4: Inter-RAT UMTS Requirements in NSA
In NSA (EN-DC) the inter-RAT UMTS requirements shall be defined to support mobility between E-UTRA FDD and UMTS, and between E-UTRA TDD and UMTS in Rel-15:
  The corresponding inter-RAT UMTS (UTRAN FDD and UTRAN TDD) requirements in NSA shall be defined in at least TS 36.133:
    The requirements shall be defined in both RRC IDLE and RRC CONNECTED states.
    Certain requirements (e.g. number of UTRA FDD/TDD layers to monitor) may also be defined in TS 38.133.