## Slide 1: WF on 256QAM for FR2
Intel Corporation
3GPP TSG-RAN WG4 Meeting AH-1801 San Diego, California, USA, 22 - 26 January 2018 Agenda Item: 4.2
R4-1801003

## Slide 2: Way Forward
  Feasibility of DL 256QAM for FR2 is FFS including feasible TX and RX EVM assumptions and performance benefits
Companies are encouraged to bring inputs on
  Performance comparison of 64QAM and 256QAM for FR2
      Focus on link-level performance comparison
      Interested companies can bring system-level evaluation results
  Feasible TX and RX EVM assumptions for 256QAM FR2
Timelines
  The decision on the introduction of 256QAM FR2 requirements in Rel-15 timeframe shall be made in RAN4 #86 (Feb’18)
    Note: this does not preclude introduction of 256QAM in the future in release-independent way
  Companies are encouraged to bring analysis in RAN4 #86. Additional results can be submitted in RAN4 #86bis.

## Slide 3: Link-level Simulation Assumptions
Carrier frequency: [29] GHz
CBW: 50 MHz
SCS: 120kHz, 60kHz
Number of allocated PRBs: 32 RPBs for 120kHz SCS, 66 PRBs for 60kHz SCS
Adaptive MCS and MIMO rank (rank 1/2) selection
  64 QAM: Throughput curves envelope for MCS index Table 1 (TS 38.214 Table 5.1.3.1-1)
  256 QAM: Throughput curves envelope for MCS index Table 2 (TS 38.214 Table 5.1.3.1-2)
Propagation conditions:
  TDL-A, 30 ns delay spread, UE speed 5 km/h;
  TDL-D, 30 ns delay spread, UE speed 5 km/h;
2x2 Low MIMO correlation
DMRS configuration:
  Option 2: Type 1, DL-DMRS-len = 1, DL-DMRS-add-pos = 2 (i.e. 3 DMRS symbols per slot)
  Option 2: Type 2, DL-DMRS-len = 2, DL-DMRS-add-pos = 1 (i.e. 4 DMRS symbols per slot)
High density PTRS: KPTRS = 2 (every 2nd RB), LPTRS = 1 (each OFDM symbol)
Receiver:
  Realistic/practical channel estimation
  Practical phase noise compensation based on PTRS
    Ideal CPE compensation is not precluded

## Slide 4: Link-level Simulation Assumptions
RF impairments:
  Scenario #1: No RF impairments (i.e. TX/RX EVM = 0%)
    Note: the scenario is used for reference purposes
  Scenario #2:
    Practical RF impairments including 2 components for TX and RX
      #1: EVM:
        Baseline: [2, 3, 4, 5, 6%]
        Optional: [1%]
      #2: Explicitly modelled Phase noise for TX and RX
    Notes:
      The assumptions do not imply tightening 64QAM EVM requirements
      Baseline: Same EVM between 64QAM and 256QAM
      Additional results with higher EVM for 64QAM can be provided
      Same EVM assumed for TX and RX
    Phase noise models for analysis:
      TR 38.803 Example 1 model (section 6.1.10)
      TR 38.803 Example 2 model (section 6.1.11)
      Other phase noise model is not precluded