## Slide 1: WF on wideband operation of NR UE
LG Electronics
R4-1801006
3GPP TSG-RAN WG4 #AH-1801 Meeting
San Diego, California, USA, Jan. 22 – 26, 2018
Agenda: 4.2.1

## Slide 2: Background (1)
In RAN4 #85 meeting, RAN4 has agreed the UE behavior and UE RF requirements for wideband operation.
  UE behavior
    The UE meets RF requirements related to it’s configured BWP according to UE CBW (no additional BWP related RF requirements)
      FFS whether UE CBW next highest value after BWP bandwidth
    How the UE configures it’s RF in order to operate the BWP and meet the CBW based RF requirements is implementation dependent
  UE RF requirements
    Single BWP case: single CC RF requirements apply with UE CC BW
    Multiple BWPs case : intra-band CA RF requirements apply with UE CC BW

## Slide 3: Background (2)
UE behavior: BWP configured w/ smaller PRBs compared to UE CC BW
  Option1: Do not change the UE operating CC BW even if the configured BWP is less than UE configured CC BW
  Option2: Changed the UE operating CC BW according to the new allocated BWP

## Slide 4
UE behavior
  UE can be configured a BWP with small PRBs less than UE CC Bandwidth.
  UE RF requirements for DL and UL are applied based on configured UE CC bandwidth even if any BWPs less than configured UE CC bandwidth is configured
    As UE implementation aspect, Option 2 in slide 3 is not precluded
  RAN4 will only apply the requirements according to set of UE CBW.
  It is FFS if UE can be configured BWP with RB granularity. If RAN4 agreed UE cannot be configured BWP with RB granularity, LS can be sent to RAN1
Way Forward (1)

## Slide 5
UE RF requirements for wideband operation
  For Multiple BWPs case, the related RF requirements will be studied in intra-band NR CA Work.
    E. g.) Bandwidth class, MPR, configured Tx power, SEM, REFSENS…
Way Forward (2)