## Slide 1: WF on NR CACLR requirement for non-continuous allocation
Nokia, Nokia Shanghai Bell, ZTE, NTT DOCOMO
3GPP TSG-RAN WG4 Meeting AH-1801
San Diego, California, USA, 22 – 26 January 2018
Agenda Item: 4.4.2.5.1.2
R4-1801020

## Slide 2: Background
Contributions on NR BS CACLR requirement for non-continuous allocation have been discussed in RAN4 AH-1801:
  [1] R4-1800529 Further discussion on NR CACLR requirement ZTE
  [2] R4-1800673 OTA ACLR for non-contiguous spectrum and multiple band operation in FR1 and FR2 NR BS NTT DOCOMO, INC.

## Slide 3: Way forward on BS type 1-C / 1-H CACLR
To clarify the BS type 1-C and 1-H CACLR requirement in non-contiguous spectrum or multiple bands by modifying table 6.6.3.2-3 in clause 6.6.3.2:
Channel bandwidth of NR lowest/highest carrier transmitted BWChannel [MHz] | Sub-block or Inter RF Bandwidth gap size (Wgap) where the limit applies | BS adjacent channel centre frequency offset below or above the sub-block edge or the Base Station RF Bandwidth edge (inside the gap) | Assumed adjacent channel carrier | Filter on the adjacent channel frequency and corresponding filter bandwidth | ACLR limit
5, 10, 15, 20 | 5 MHz ≤ Wgap < 15 MHz (Note 2) 5 MHz ≤ Wgap < 45 MHz (Note 3) | 2.5 MHz | 5 MHz NR with SCS that provides largest transmission bandwidth configuration (BWConfig) | Square (BWConfig) | 45 dB
 | 10 MHz < Wgap < 20 MHz (Note 2) 10 MHz ≤ Wgap < 50 MHz (Note 3) | 7.5 MHz | 5 MHz NR with SCS that provides largest transmission bandwidth configuration (BWConfig) | Square (BWConfig) | 45 dB
[25, 30, 40, 50, 60, 70, 80,90, 100] | 20 MHz ≤ Wgap < 60 MHz (Note 3) 20 MHz ≤ Wgap < 30 MHz (Note 2) | 10 MHz | 20 MHz NR with SCS that provides largest transmission bandwidth configuration (BWConfig) | Square (BWConfig) | 45 dB
 | 40 MHz < Wgap < 80 MHz (Note 3) 40 MHz ≤ Wgap < 50 MHz (Note 2) | 30 MHz | 20 MHz NR with SCS that provides largest transmission bandwidth configuration (BWConfig) | Square (BWConfig) | 45 dB
NOTE 1: BWConfig is the transmission bandwidth configuration of the assumed adjacent channel carrier. NOTE 2: Applicable in case the BWChannel of NR carrier transmitted at the other edge of the gap is 5, 10, 15, 20 MHz. NOTE 3: Applicable in case the BWChannel of NR carrier transmitted at the other edge of the gap is [25, 30, 40, 50, 60, 70, 80,90, 100] MHz. |  |  |  |  | 

## Slide 4: Way forward on BS type 1-C / 1-H ACLR
To clarify the BS type 1-C and 1-H ACLR requirement in non-contiguous spectrum or multiple bands by adding table 6.6.3.2-5 in clause 6.6.3.2:
Channel bandwidth of NR lowest/highest carrier transmitted BWChannel [MHz] | Sub-block or Inter RF Bandwidth gap size (Wgap) where the limit applies | BS adjacent channel centre frequency offset below or above the sub-block edge or the Base Station RF Bandwidth edge (inside the gap) | Assumed adjacent channel carrier | Filter on the adjacent channel frequency and corresponding filter bandwidth | ACLR limit
5, 10, 15, 20 | Wgap ≥ 15 MHz (Note 2) Wgap ≥ 45 MHz (Note 3) | 2.5 MHz | 5 MHz NR with SCS that provides largest transmission bandwidth configuration (BWConfig) | Square (BWConfig) | 45 dB
 | Wgap ≥ 20 MHz (Note 2) Wgap ≥ 50 MHz (Note 3) | 7.5 MHz | 5 MHz NR with SCS that provides largest transmission bandwidth configuration (BWConfig) | Square (BWConfig) | 45 dB
[25, 30, 40, 50, 60, 70, 80,90, 100] | Wgap ≥ 60 MHz (Note 3) Wgap ≥ 30 MHz (Note 2) | 10 MHz | 20 MHz NR with SCS that provides largest transmission bandwidth configuration (BWConfig) | Square (BWConfig) | 45 dB
 | Wgap ≥ 80 MHz (Note 3) Wgap ≥ 50 MHz (Note 2) | 30 MHz | 20 MHz NR with SCS that provides largest transmission bandwidth configuration (BWConfig) | Square (BWConfig) | 45 dB
NOTE 1: BWConfig is the transmission bandwidth configuration of the assumed adjacent channel carrier. NOTE 2: Applicable in case the BWChannel of NR carrier transmitted at the other edge of the gap is 5, 10, 15, 20 MHz. NOTE 3: Applicable in case the BWChannel of NR carrier transmitted at the other edge of the gap is [25, 30, 40, 50, 60, 70, 80,90, 100] MHz. |  |  |  |  | 

## Slide 5: Way forward on BS type 1-C / 1-H ACLR / CACLR
To clarify the BS type 1-C / 1-H ACLR / CACLR requirement in non-contiguous spectrum or multiple bands by modifying two paragraphs in clause 6.6.3.1:
[For a BS operating in non-contiguous spectrum, the ACLR requirement in subclause 6.6.3.2 applies in sub block gaps for the frequency ranges defined in table 6.6.3.2-5, while CACLR requirement in subclause 6.6.3.2 applies in sub block gaps for the frequency ranges defined in table 6.6.3.2-3.
For a BS operating in multiple bands, where multiple bands are mapped onto the same antenna connector, the ACLR requirement in subclause 6.6.3.2 applies in sub block gaps for the frequency ranges defined in table 6.6.3.2-5, while CACLR requirement in subclause 6.6.3.2 applies in Inter RF Bandwidth gaps for the frequency ranges defined in table 6.6.3.2-3.]

## Slide 6: Way forward on BS type 1-O ACLR / CACLR
To clarify the BS type 1-O ACLR /CACLR requirement in non-contiguous spectrum or multiple bands by adding three paragraphs in clause 9.7.3.2:
The OTA ACLR(CACLR) basic limit or the OTA ACLR absolute limit, whichever is less stringent, shall apply, unless stated otherwise in regional regulation.
For a RIB operating in non-contiguous spectrum, the ACLR requirement in subclause 6.6.3.2 applies in sub block gaps for the frequency ranges defined in table 6.6.3.2-5, while the CACLR requirement in subclause 6.6.3.2 applies in sub block gaps for the frequency ranges defined in table 6.6.3.2-3.
For a RIB operating in multiple bands, the ACLR requirement in subclause 6.6.3.2 applies in sub block gaps for the frequency ranges defined in table 6.6.3.2-5, while the CACLR requirement in subclause 6.6.3.2 applies in Inter RF Bandwidth gaps for the frequency ranges defined in table 6.6.3.2-3.

## Slide 7: Way forward on BS type 2-O ACLR / CACLR
To further discuss (considering the different channel bandwidth combinations of the NR carriers transmitted) and decide in RAN4#86:
The applicable OTA ACLR requirement within the sub-block or Inter RF Bandwidth gap for NR BS type 2-O operating in non-contiguous spectrum or multiple bands.
The applicable OTA CACLR requirement within the sub-block or Inter RF Bandwidth gap for NR BS type 2-O operating in non-contiguous spectrum or multiple bands.