## Slide 1: WF on FR2 UEM
Agenda Item: 4.4.2.5.2
Document for: Approval
Source: Ericsson
3GPP TSG-RAN WG4 AH-1801 Tdoc R4-1801024
San Diego, CA, US, 22 – 26 January, 2018

## Slide 2: Background
The unwanted emissions are for BS type 2-O expressed as an OTA spectrum emission mask (transmission centric), fundamentally based on the ITU-R IMT-2020 parameters and related to the PTx level of the BS
Several open issues remain in TS 38.104 (Editor’s notes):
  How to account for the “OOB boundary” (“250% rule”)
  Definition and implication of “total transmission boundary”
  Type of emission mask and frequency range (carrier centric or band centric)
  Emission limits and corresponding power levels
  Relation to spurious emission limits, where presently only a general level of -13 dBm is accounted for
  Criteria to classify the requirement

## Slide 3: Inputs and proposals
Make FR2 SEM BS class (deployment scenario) specific rather than power level specific [1]
Keep FR2 SEM TRP (PTx) specific, PTx defined as Rated TRP output power declared per RIB [3]
Using a more realistic 29 dBm power level threshold instead o 35 dBm [2]
Define Total transmission BW to cover multiple contiguous carriers [3]
Base OOB boundary on ITU-R SM.1539 [3]
Introduce Notes on Non-contiguous and MB operation [4]
For lower power levels and BW<200 MHz, introduce a mask with 5 dB higher limits [4]

## Slide 4: Agreements
Based on present spectrum situation in FR2
  Requirements should cover non-contiguous spectrum operation in Rel-15
  Multiband operation is for future study in FR2
  NOTE: Above agreement concerns all FR2 RF requirements.
Definition of Total transmission BW
  Covers contiguous multicarrier transmissions
  NOTE: There may be variations in regional applicability.
We need to conclude the requirement in February

## Slide 5: Open issues for study
Type of emission mask and frequency range (Carrier centric (SEM) vs. band centric (UEM))
  Considering impact from possible stricter Category B limits
  Consider OOB boundary (based on regulation)
Classification of masks and relation to PTx
  Option 1: Consider to use BS classification instead of PTx for classification
    Further consider relationship between mask and PTx
  Option 2: Classify based on PTx (as now)
    Consider realistic PTx levels
    Introduce definition of PTx, based on declaration or measurements
Mask levels
  Impact from choice of mask and classification (as outlined above)
  Consider levels used by ITU-R in compatibility studies
  Consider other channel BW than 200 MHz
Definition of Total transmission BW for non-contiguous multicarrier

## Slide 6: Reference input documents
R4-1800204, "FR2 BS OOBE requirement" (Samsung).
R4-1800283, "On PTX for mm-wave UEM (FR2)" (Ericsson).
R4-1800674, "SEM for FR2 NR BS" (NTT DOCOMO, INC.).
R4-1800929, "FR2 spectrum mask" (Nokia, Nokia Shanghai Bell).
R4-1800955, "Draft CR to TS 38.104 clause 9.7.4.3 OTA spectrum emission mask" (Nokia, Nokia Shanghai Bell).