## Slide 1: WF on NR BS RF FRCs
Ericsson, Huawei, ZTE, CATT, Nokia, Nokia Shanghai Bell
3GPP TSG-RAN WG4 RAN4#85
San Diego, CA, USA, January 22nd -26th, 2018
R4-1801031
Document for: Approval

## Slide 2: Background
Based on the agreed simulations assumptions during last RAN4#85 meeting and emails exchanged, based on the updated WF R4-1714137, companies provided simulations results (see References slide for the complete list)
Following two slides capture companies’ results.

## Slide 3: Background Simulation results for REFSENS and ICS SNR

## Slide 4: Background: Simulation results for Dynamic Range SNR

## Slide 5: Observations
The targeted and effective coding rates used for those simulations are not included in the MCS tables specified by RAN1 (TS 38.214)
Assumptions related to target coding rate shall be revisited.

## Slide 6: Agreements
Following slides capture agreed simulation assumptions and TBS

## Slide 7: Simulation assumptions - DMRS
DMRS pattern type 1:
  1 symbol front loaded + 1 additional
  No FDM, no data in DMRS symbol

## Slide 8: Simulation assumptions
Receiver type: MMSE

## Slide 9: Simulation assumptions - PTRS
No PTRS for FR1
For FR2, following PTRS parameters:
  KPTRS : 2 (PTRS every 2 RBs)
  LPTRS : 1 (all symbols with PTRS)
  No phase noise simulation, PTRS REs are not used for data

## Slide 10: REFSENS and ICS assumptions
Parameter | Value
Propagation | AWGN
Modulation | QPSK
Coding rate | 1/3
Symbol type | CP-OFDM
HARQ | None
#antenna | 1
Channel estimation | practical
Criteria | SNR at 95% throughput

## Slide 11: Dynamic Range assumptions
Parameter | Value
Propagation | AWGN
Modulation | 16QAM
Coding rate | 2/3
Symbol type | CP-OFDM
HARQ | None
#antenna | 1
Channel estimation | practical
Criteria | SNR at 95% throughput

## Slide 12: TBS for FRC
TBS and CB CRCs shall be calculated as follow:
  BG:
    For code rate ≤ 1/4, BG2 is selected；
    For 1/4 ＜code rate≤ 2/3, BG2 is selected if TBS≤3824（without CRC）
    For TBS ≤ 292, BG2 is selected
    Otherwise, BG1 is selected
  TB CRC:
    24bits if TB size>3824, 16bits if TB size ≤3824；
  CB CRC:
    24bits;
TBS size shall be given without CRC (payload only).

## Slide 13: Agreements
SNR values (practical channel estimation) shall be provided for next February RAN4#86 meeting.
No margin should be included.

## Slide 14: MCS index and target coding rate
  REFSENS and ICS:
    MCS index = 4
    Target coding rate = 308/1024
  Dynamic Range:
    MCS index = 16
    Target coding Rate = 658/1024

## Slide 15: REFSENS and ICS TBS: MCS=4

## Slide 16: Dyn Range TBS: MCS=16

## Slide 17: Implementation margin
For REFSENS and ICS:
  IM = 2dB
For Dynamic Range
  IM = 2.5 dB

## Slide 18: Way forward
Companies are encouraged to provide simulation results for next RAN4#86.
SNR value for each FRC shall be specified by RAN4#86.

## Slide 19: References
[1] R4-1800496, Simulation results for NR BS REFSENS and ICS SNR for FR, Huawei
[2] R4-1800497, Simulation results for NR BS REFSENS and ICS SNR for FR2,Huawei
[3] R4-1800038, Simulation results for NR BS receiver sensitivity SNR, CATT
[4] R4-1800044, Simulation results for ICS SNR, CATT
[5] R4-1800532, updated simulation results for FR1 REFSENS requirement, ZTE
[6] R4-1800533, updated simulation results for FR2 OTA REFSENS requirement, ZTE
[7] R4-1800537, Updated simulation results for FR1 ICS requirement , ZTE
[8] R4-1800539, Updated simulation results for FR2 ICS requirement, ZTE
[9] R4-1800024, Simulation Results for FRC for BS receiver reference sensitivity requirements,Nokia
[10] R4-1800029, Simulation Results for FRC for BS receiver in-channel sensitivity requirements, Nokia
[11] R4-1800329, Simulations results FRCs REFSENS FR1,Ericsson
[12] R4-1800330, Simulations results FRCs REFSENS FR2,Ericsson
[13] R4-1800331, Simulations results Additional FRCs ICS FR1,Ericsson
[14] R4-1800332, Simulations results Additional FRCs ICS FR2,Ericsson
[15] R4-1800498, Simulation results for NR BS Dynamic Range SNR,Huawei
[16] R4-1800039, Simulation results for NR BS dynamic range SNR,CATT
[17] R4-1800541, Updated simulation results for FR1 dynamic range requirement,ZTE
[18] R4-1800025, Simulation Results for FRC for BS receiver dynamic range requirements,Nokia
[19] R4-1800333, Simulations results FRCs Dynamic Range FR1,Ericsson