## Slide 1
3GPP TSG-RAN WG4 Meeting AH-1801 R4-1801042
San Diego , US, 22 - 26 Jan, 2018
Agenda Item: 4.6.1
WF on RRM requirements for SA operation
CMCC, ZTE

## Slide 2: Overall RRM requirements (1)
 |  | Agreement | 
Types | Functionality | Requirement is needed or not for SA | Whether NSA requirements can be reused for SA operation
RRC_IDLE state mobility | cell selection | Not needed | N/A
 | Paging interruption | needed | Define new requirements
 | Measurement capability | needed | Reuse NSA agreements Note: The number of frequency layers could reuse the agreements of NSA operation, but the requirements architecture need to be updated
 | Cell reselection, including intra-frequency, inter-frequency and inter-RAT | needed | Define new requirements
RRC_INACTIVE state mobility (Note 1) | Measurement capability | needed | Reuse NSA agreements Note: The number of frequency layers could reuse the agreements of NSA operation, but the requirements architecture need to be updated
 | Paging interruption | needed | Define new requirements
 | Cell reselection, including intra-frequency, inter-frequency and inter-RAT | needed | Define new requirements
  Note1:
  The detailed requirements may be similar with idle mode pending RAN2 progress

## Slide 3: Overall RRM requirements (2)
 |  | Agreement | 
Types | Functionality | Requirement is needed or not for SA | Whether NSA requirements can be reused for SA operation
RRC_CONNECTED state mobility | Handover | needed | Define new requirements
 | RRC re-establishment | needed | Define new requirements
 | RRC connection release with redirection | needed | Define new requirements
 | Random access | needed | Reuse NSA agreements Note : update may be needed based on RAN1/RAN2 progress
Timing | UE transmit timing | needed | Reuse NSA agreements
 | timer accuracy | needed | Reuse NSA agreements
 | timing advance | needed | Reuse NSA agreements
 | cell phase synchronization accuracy | needed | Reuse NSA agreements
 | NR CA MRTD | needed | Reuse NSA agreements
 | NR CA MTTD | needed | There is no MTTD requirement yet for NSA . The unified requirements can be specified for SA and NSA
 | NR DC MRTD | FFS (Note: NR-NR DC is in the Rel-15 scope, but whether to specify requirements is based on RF progress on NR-NR DC combinations) | 
 | NR DC MTTD |  | 

## Slide 4: Overall RRM requirements (3)
 |  | Agreement | 
Types | Functionality | Requirement is needed or not for SA | Whether NSA requirements can be reused for SA operation
signalling | Radio link monitoring | needed | Reuse NSA agreements
 | NR PSCell addition/release delay | FFS (Note: NR-NR DC is in the Rel-15 scope, but whether to specify requirements is based on RF progress on NR-NR DC combinations) | 
 | NR SCell Activation and Deactivation Delay | needed | Reuse NSA agreements
 | Interruption | needed | There is no interruption requirements yet for NSA . The unified requirements can be specified for both SA and NSA PSCell.
 | SUL carrier RRC reconfiguration delay | needed | Reuse NSA agreements
Measurement procedure | Measurement capability | needed | Reuse NSA agreements Note: the number of frequency layers could reuse the agreements of NSA operation, but the requirements architecture need to be updated
 | Intra/inter measurement, including cell detection | needed | Reuse NSA agreements
 | Inter-RAT measurement, including cell detection | needed | Define new requirements
 | Measurement gap | needed | Reuse NSA agreements Note: the applicability rule need to be updated
 | Event triggering and reporting criteria | needed | Define new requirements
Measurement performance requirement | Measurement accuracy | needed | There is no accuracy requirements yet for NSA . The unified requirements can be specified for SA and NSA. Note: the requirements will be specified in the performance phase of the work item