## Slide 1: Way forward on UE behavior during measurement outside measurement gap
NTT DOCOMO
R4-1801053
Document for: Approval
3GPP TSG-RAN WG4 NR-AH#4
San Diego, US, January 22nd - January 26th, 2018
Agenda item: 4.6.4.2

## Slide 2: Updated proposal
Within a SMTC window which is not overlapped with measurement gap in non-CA case:
In FR1 intra-frequency SS-RSRP/RSRQ/SINR measurement:
  For UE not supporting mixed numerology scenarios, UE is not expected to transmit PUCCH/PUSCH or receive PDCCH/PDSCH on SSB symbols to be measured, [1] symbol before each consecutive SSB symbols and [1] symbol after each consecutive SSB symbols within SMTC window duration if useServingCellTimingForSync is enabled
  For UE not supporting mixed numerology scenarios, UE is not expected to transmit PUCCH/PUSCH or receive PDCCH/PDSCH on all symbols within SMTC window duration if useServingCellTimingForSync is not enabled
In FR2 intra-frequency SS-RSRP/SINR measurement:
  UE is not expected to transmit PUCCH/PUSCH or receive PDCCH/PDSCH on SSB symbols to be measured, X symbol(s) before each consecutive SSB symbols and X symbol(s) after each consecutive SSB symbols within SMTC window duration (assuming that useServingCellTimingForSync is always enabled for FR2)
In FR2 intra-frequency SS-RSRQ measurement:
  UE is not expected to transmit PUCCH/PUSCH or receive PDCCH/PDSCH on SSB symbols to be measured , RSSI measurement symbols, X symbol(s) before each consecutive SSB/RSSI symbols and X symbol(s) after each consecutive SSB/RSSI symbols within SMTC window duration (assuming that useServingCellTimingForSync is always enabled for FR2)
Note: whether or not to define specific behavior for rate matching around above symbols is up to RAN1
Note: RAN4 needs to check if cell synchronization accuracy complies with cell phase synchronization requirement in TS 38.133 when useServingCellTimingForSync is enabled
X = [1]
  Companies are encouraged to check whether above X value is feasible or not
  If X is revisited and it becomes large value e.g., more than 4, following alternative solutions should be considered
    SMTC-based solution, i.e., all symbols within SMTC window are not available
    SSB-slot-based solution, i.e., all symbols within slot(s) containing SSB are not available

## Slide 3: Updated proposal
Within a SMTC window which is not overlapped with measurement gap in CA case:
In FR1 intra-frequency SS-RSRP/RSRQ/SINR measurement for intra-band CA without UE capability on simultaneous reception of SSB and data with mixed numerologies,
  in each serving cell, UE is not expected to transmit PUCCH/PUSCH or receive PDCCH/PDSCH on SSB symbols to be measured, [1] symbol(s) before each consecutive SSB symbols and [1] symbol(s) after each consecutive SSB/RSSI symbols for any one of intra-frequency measurements if the SSB to be measured has different SCS from that for serving cell data and useServingCellTimingForSync is enabled
  in each serving cell, UE is not expected to transmit PUCCH/PUSCH or receive PDCCH/PDSCH on all symbols within SMTC window duration for any one of intra-frequency measurements if the SSB to be measured has different SCS from that for serving cell data and useServingCellTimingForSync is not enabled
In FR2 intra-frequency SS-RSRP/SINR measurement for intra-band CA,
  in each serving cell, UE is not expected to transmit PUCCH/PUSCH or receive PDCCH/PDSCH on SSB symbols to be measured, X symbol(s) before each consecutive SSB symbols and X symbol(s) after each consecutive SSB symbols for any one of intra-frequency measurements
In FR2 intra-frequency SS-RSRQ measurement for intra-band CA,
  in each serving cell, UE is not expected to transmit PUCCH/PUSCH or receive PDCCH/PDSCH on SSB symbols to be measured , RSSI measurement symbols, X symbol(s) before each consecutive SSB/RSSI symbols and X symbol(s) after each consecutive SSB/RSSI symbols within SMTC window duration for any one of intra-frequency measurements (assuming that useServingCellTimingForSync is always enabled for FR2)

## Slide 4: Updated proposal
NR supports to configure enabling/disabling intra-frequency measurement on each NR SCell
  When there is at least one serving cell with intra-frequency measurement within serving cells for intra-band CA, disabling intra-frequency measurement on other serving cell(s) is possible
  Detailed signaling design is up to RAN2

## Slide 5: [Appendix] Discussion
Regarding RX beam switching time, basically all UEs capable of FR2 operation should be able to perform fast RX beam switching
  Otherwise, PDSCH reception after PDCCH reception does not work in the case where PDCCH beam and PDSCH beam are different (it is not minor case)
Since the number of cell searchers at UE would be limited, there is a concern on measurement requirements for the case where SMTC window timings across different intra-freq/inter-freq carriers to be measured are overlapped.
  If SMTC on each serving CC is not aligned as in Case 1, measurement can be performed for each CC in corresponding SMTC timing. However, mixed numerology or analog Rx beam restriction would happen even when measuring other CC (e.g., intra-band CC)
  If SMTC on each serving CC is aligned as in Case 2, measurement would be performed for each CC in different timings. Even in such case, mixed numerology or analog Rx beam restriction would happen e.g., across intra-band CCs
Case 1
Serving #0
Serving #1
Serving #2
Inter-freq
MG
SMTC
SMTC
OK
OK
OK
OK
OK
OK
Case 2
SMTC
OK
OK
SMTC
OK
SMTC
OK
OK
OK
MG

## Slide 6: [Appendix] Discussion
For intra-band CA operation, intra-frequency measurement on only one of serving CCs would be enough in some cases (e.g., co-located CCs)
  Hence, it should be possible to disable intra-frequency measurement on other serving CCs
  It is beneficial not only for case with mixed numerology and/or analog BF restriction but also for general measurement delay for overlapped SMTCs
When there are multiple serving CCs with intra-frequency measurement for intra-band CA, UE would not be able to receive PDSCH/PDCCH during measurement on any one of CCs due to mixed numerology and/or analog BF restriction
CC#1
CC#2
e.g., 3 ms SMTC window with actual SSB index {#1, #3, …, #31} for measurement
e.g., 1 ms SMTC window with actual SSB index {#0, #1, …, #15} for measurement
Not available for data reception on CC#1 due to measurement on CC#2
Not available for data reception on CC#2 due to measurement on CC#1