## Slide 1: Way forward on Intra-frequency Cell Identification Requirements without Gap
Intel
3GPP TSG-RAN WG4 Meeting AH-1801 San Diego, US, 22-26 January 2018
R4-1801055

## Slide 2: Background
In TS 38.133 there are 2 sets of requirements for cell identification for intra-frequency measurements without gap:
  The UE shall be able to identify a new detectable intra frequency cell within Tidentify_intra_without_index if the UE has already identified an SS block with different time index and the same physical cell ID, or the UE has been indicated that the neighbour cell is synchronous with the serving cell. Otherwise UE shall be able to identify a new detectable intra frequency cell within Tidentify_intra_with_index
  Tidentify_intra_without_index = TPSS/SSS_sync + T SSB_measurement_period ms
  Tidentify_intra_with_index = TPSS/SSS_sync + T SSB_measurement_period + TSSB_time_index ms
  TPSS/SSS_sync - the PSS/SSS detection delay
  T SSB_measurement_period - the measurement period of SSB based measurement
  TSSB_time_index - the SSB Index acquisition delay
Two issues had been extensively discussed in the RAN4 AH 1801 Meeting:
1. The forms of formulas to represent these time requirements;
2. The “assumed maximum number of Rx beams” to be is adopted for requirement definition purpose.
Note: the requirement is for intra-frequency “without gap”, without considering the SMTC occasions are partially/fully overlapped with measurement gap and without considering multiple CC scenarios.

## Slide 3: Background (Formulas for FR1)
For FR1, consensus could be reached to use a unified formula form for TPSS/SSS_sync, T SSB_measurement_period
and TSSB_time_index as below
max([a constant value], [number of SSB] x SMTC_period)
In addition, it has already been agreed to apply 600ms and 200ms in the constant value part to
TPSS/SSS_sync and T SSB_measurement_period, respectively. Therefore,
Proposal 1: For FR1, it is proposed to set TPSS/SSS_sync, T SSB_measurement_period and TSSB_time_index requirement as:
TPSS/SSS_sync = max( 600, [5 or 6] x SMTC_period ) ms (1)
TSSB_time_index = max( [TBD], [2+X] x SMTC_period ) ms (2)
TSSB_measurement_period = max( 200, [5] x SMTC_period ) ms (3)

## Slide 4: Proposed Form of Formulas for FR2
For FR2, consensus could be reached to use a parameter N related to Rx beamforming and Rx beam sweeping for requirement definition purpose, but the value of N is TBD.
In addition, it is also TBD if N should be the same value or not for different processes, including PSS/SSS detection, SSB time index detection and SSB measurement processes.
So far, there are two options on the form of the formulas:
Option 1: max( [a constant value], [number of SSB] x N x SMTC_period )
Option 2: N x max( [a constant value], [number of SSB] x SMTC_period )

## Slide 5: Proposed Form of Formulas for FR2
In order to ensure acceptable mobility performance from system perspective and acceptable power consumption from UE perspective, it is important to guarantee a constant value in the time delay requirement without the impact by other factors.
In addition, in order to maintain a consistent form of the requirement formulas as in FR1, it is proposed that
Proposal 2: For FR2, requirements of TPSS/SSS_sync, T SSB_measurement_period and TSSB_time_index are given as in Option 1:
TPSS/SSS_sync = max( [X1], [Y1] x N1 x SMTC_period ) ms (4)
TSSB_time_index = max( [X2], [3+Y2] x N2 x SMTC_period ) ms (5)
TSSB_measurement_period = max( [X3], [Y3] x N3 x SMTC_period ) ms (6)
Proposal 3: Interested companies are encouraged to propose [TBD] values in formulas (1) to (6), and the parameter N related to Rx beamforming and Rx beam sweeping in formulas (4) to (6).

## Slide 6: Appendix A:
In order to better align the proposed values from different companies, as an example, interested companies are encouraged to provide requirement values according to the parameters listed in the table below, upon the agreed requirement formulas in this WF.
For example: For FR2, TPSS/SSS_sync = max( [X1], [Y1] x N1 x SMTC_period ) ms
 | Constant value X1 | Number of SSB Y1 | Parameter N1
Company 1 |  |  | 
Company 2 |  |  | 
… |  |  | 
Consensus value |  |  |