## Slide 1: Way forward on CSI-RS based measurement in NR
Huawei, HiSilicon,
3GPP TSG-RAN WG4 Meeting AH-1801 R4-1801059
San Diego, USA, January22nd – 26th, 2018
Agenda Item: 4.6.5

## Slide 2: CSI-RS based measurement reporting delay
For CSI-RS based measurement, the requirements on measurement reporting delay can be defined as:
Treporting_delay_CSI-RS= Tsearch + TCSI-RS_measurement_period
  If associated SSB is configured, Tsearch is the time period to identify the associated SSB
  If associated SSB is not configured, Tsearch is the time period to identify any SSB of the corresponding cell with SSB index reading.
  TCSI_RS_measurement_period is the measurement period of CSI-RS based measurement.

## Slide 3: Search time for the associated SSB
Case 1: When associated SSB is configured for a CSI-RS resource for mobility and the associated SSB is detectable.
  Case 1-1: The UE has been indicated that the corresponding cell is synchronous with the serving cell
    Tsearch = TPSS/SSS_sync
  Case 1-2: The UE has not been indicated that the corresponding cell is synchronous with the serving cell
    Tsearch = TPSS/SSS_sync + TSSB_time_index
  Side condition: SINR of the associated SSB is higher than [-6]dB

## Slide 4: Search time for any SSB of corresponding cell
Case 2: When associated SSB is not configured for a CSI-RS resource for mobility and any SSB of the corresponding cell is detectable.
  Case 2-1: The UE has been indicated that the corresponding cell is synchronous with the serving cell
    Tsearch = TPSS/SSS_sync
  Case 2-2: The UE has not been indicated that the corresponding cell is synchronous with the serving cell
    Tsearch = TPSS/SSS_sync + TSSB_time_index
  Side condition: SINR of any SSB of the the corresponding cell is higher than [-6]dB

## Slide 5: Consensus
The requirements on TPSS/SSS_sync and TSSB_time_index applied for SSB based measurements can be reused for CSI-RS based measurements.
RAN4 need to study the measurement period and measurement accuracy of CSI-RSRP/CSI-RSRQ/CSI-SINR