## Slide 1: WF on inter-RAT SFTD measurement for EN-DC capable UE
Ericsson, NTT Docomo, …
R4-1801062
3GPP RAN WG4 Radio #AH-1801
San Diego, California, US, January 22 – 26, 2016

## Slide 2: Background
RAN2 has decided that inter-RAT SFTD measurements is to be supported by EN-DC capable UE
The use case presented by operator concerns timing drift between LTE system and NR system
Timing drift between the LTE system and the NR system may lead to outdated information on the timing offset between an LTE PCell and NR neighbor cells
Knowledge about the timing offset is needed in order for the LTE PCell to configure measurement gaps for NR inter-RAT measurements

## Slide 3: Agreements
Inter-RAT SFTD measurement for EN-DC capable UE comprises:
  Cell detection over all possible SSB timings in an SMTC period
  MIB acquisition
Inter-RAT SFTD measurement configuration contains at least the following:
  NR carrier frequency
  SMTC period length
Inter-RAT SFTD measurement report contains:
  SFTD for strongest detected NR neighbor cell (criterion FFS)
  PCI of detected cell

## Slide 4: Agreements
Inter-RAT SFTD core requirements shall not drive UE hardware complexity:
  Assumption on minimum NR cell search processing capacity: 5ms radio time at most every 20ms
Architectures and scenarios to consider:
  Receiver for NR available (cf. LTE CA non-contiguous case)
  Receiver for NR currently occupied by LTE SCC reception (LTE CA) (Responsibility of PCell to avoid resource conflict)
  Shared receiver for LTE and NR (cf. LTE CA intra-band contiguous case)

## Slide 5: Agreements
Measurement execution:
  Measurements conducted without support of measurement gaps
  Interruptions for radio reconfiguration are allowed
Side conditions:
  Favorable conditions, e.g. SINR > -3dB

## Slide 6: For RAN4#86
Companies are encouraged to provide the following:
  Analysis of acquisition time and interruptions needed for inter-RAT SFTD as function of SMTC period and receiver architecture
  Criterion for strongest detected cell
  Tentative definition for inter-RAT SFTD measurement (to provide to RAN1)