## Slide 1: Way forward on handover
Huawei, HiSilicon, Nokia, Nokia Shanghai Bell, …
3GPP TSG-RAN WG4 Meeting AH-1801 R4-1801065
San Diego, USA, January 22nd – 26th, 2018
Agenda Item: 4.6.9

## Slide 2: Agreement
Handover RRM requirements should be defined to cover following scenarios:
  Handover from NR to NR
    To be captured in TS38.133
  Handover from NR to E-UTRAN
    To be captured in TS38.133
  Handover from E-UTRAN to NR
    To be captured in TS36.133
Generic requirements can be defined in TS38.133 to cover both FDD and TDD NR source/target cells.
The equations of Dhandover and Tinterrupt in following slides apply for target cells in both FR1 and FR2. However, the components in Tinterrupt are expected to have different values in FR1 and FR2.

## Slide 3: Agreement
Handover delay and interruption time should be defined
Handover delay Dhandover is defined from the time when the UE receives a RRC message implying handover to the time when UE shall be ready to start the transmission of the new uplink PRACH channel:
  Dhandover = TRRC_procedure_delay + Tinterruption
Where:
  TRRC_procedure_delay: it is the RRC procedure delay defined TS 38.331
  Tinterruption: it is the time between end of the last TTI containing the RRC command on the old PDSCH and the time the UE starts transmission of the new PRACH, excluding TRRC_procedure_delay.

## Slide 4: Handover from NR to NR
  Tinterrupt shall be defined in TS38.133
    Tinterrupt = Tsearch + TIU + Tprocessing_NR + TMIB + [Tloops] ms
  Where:
    Tsearch: is the time for PSS/SSS detection, which is 0 for known cell. aAnd [TBD] ms for unknown cell provided that the signal quality is sufficient for successful cell detection on the first attempt
    TIU: is the interruption uncertainty in acquiring the first available PRACH occasion in the new cell. TIU can be up to [TBD] ms.
    Tprocessing_NR: is the UE processing time, which can be up to [TBD]ms
    TMIB: is the time to required to decode MIB. MIB decoding maybe required for SFN or Half-frame indicator. It will be zero if SFN is known and Half-frame indicator is not needed. Otherwise, it is [1]*SMTC provided that MIB can be decoded in the first attempt.
    [Tloops]: is time for time refinement, which is up to [TBD] ms
      Note: whether [Tloops] is needed is FFS.

## Slide 5: Handover from NR to E-URTAN
  Tinterrupt shall be defined in TS38.133
    Tinterrupt = Tsearch + TIU + Tprocessing_NR2LTE ms
  Where:
    Tsearch: is the time for PSS/SSS detection, which is 0 for known cell and 80ms for unknown cell provided that the signal quality is sufficient for successful cell detection on the first attempt
    TIU: is the interruption uncertainty in acquiring the first available PRACH occasion in the new cell. TIU can be up to 30ms.
    Tprocessing_NR2LTE: is the UE processing time, which can be up to [TBD]ms

## Slide 6: Handover from E-UTRAN to NR
  Tinterrupt shall be defined in TS36.133
    Tinterrupt = Tsearch + TIU + Tprocessing_LTE2NR + TMIB + [Tloops] ms
  Where:
    Tsearch: is the time for PSS/SSS detection, which is 0 for known cell and [TBD] ms for unknown cell provided that the signal quality is sufficient for successful cell detection on the first attempt
    TIU: is the interruption uncertainty in acquiring the first available PRACH occasion in the new cell. TIU can be up to [TBD] ms.
    Tprocessing_LTE2NR: is the UE processing time, which can be up to [TBD]20ms
    TMIB: is the time to required to decode MIB. MIB decoding maybe required for SFN or Half-frame indicator. It will be zero if SFN is known and Half-frame indicator is not needed. Otherwise, it is [1]*SMTC provided that MIB can be decoded in the first attempt.
    [Tloops]: is time for time refinement, which is up to [TBD] ms
      Note: whether [Tloops] is needed is FFS.