## Slide 1: 3GPP TSG-RAN WG4 Meeting NR#3 Nagoya, Japan, 18 – 21 Sep, 2017
Huawei, …
Way forward on NR UE REFSENS SNR simulation assumptions
R4-1801072

## Slide 2: Background(1/2)
During RAN4#85 Reno meeting, WF R4-1714028, “WF on UE REFSENS simulation assumptions”, was agreed, simulation results from companies are submitted during this meeting. Further results alignments are needed.
Reference:
  R4-1800154 “NR REFSENS SNR definition”, Intel Corporation
  R4-1800969 “NR UE REFSENS SNR”, Qualcomm Incorporated
  R4-1800780 “UE RF REFSENS SNR level”, Ericsson
  Revised R4-1800203 “Discussion on UE REFSENS and updated simulation results”, Samsung
  R4-1800431 “Updated simulation results for target SNR of NR REFSENS”, LG Electronics
  R4-1801041 “Discussion on NR UE REFSENS SNR and simulation results for FR1”, Huawei, HiSilicon

## Slide 3: Background(2/2)
Simulation cases agreed in previous meeting:
  Channel bandwidth and SCS
    Provide REFSENS SNR analysis for at least for the following CBW/SCS combinations
      Set 1: FR1, 10 MHz CBW + 15 kHz SCS (52 PRBs)
      Set 2: FR1, 50 MHz CBW + 30 kHz SCS (133 PRBs)
      Set 3: FR2, 50 MHz CBW + 60 kHz SCS (66 PRBs)
    Interested companies are encouraged to provide results for following combinations
      FR1
      FR2
CBW, MHz | 5 | 10 | 15 | 20 | 25 | 40 | 50 | 60 | 80 | 100
SCS (kHz) | 15 | 15 | 15 | 15 | 30 | 30 | 30 | 60 | 60 | 60
Number of PRBs | 25 | 52 | 79 | 106 | 65 | 106 | 133 | 79 | 107 | 135
CBW, MHz | 50 | 100 | 200 | 400
SCS (kHz) | 60 | 60 | 120 | 120
Number of PRBs | 66 | 132 | 132 | 264

## Slide 4: Simulation Assumptions
PDCCH configurations:
  CORESET-freq-dom = same as the transmission bandwidth
  CORESET-time-dur = 2
DMRS configurations:
  DL-DMRS-config-type = 1
  DL-DMRS-max-len = 1
  DL-DMRS-typeA-pos=2(front-loaded DMRS pos, i.e. Symbol #2)
  Additional DMRS config:
    DL-DMRS-add-pos = 2 (Symbol #6, #9)
  DMRS and Data FDMed:
    No (exclude 12 REs for DMRS symbol)

## Slide 5: Simulation Assumptions
MCS
  MCS 4, Target code rate = 0.30 (308/1024)
PTRS configuration
  FR1: No PTRS
  FR2 :
    Option 1: No PTRS
    Option 2: PTRS is configured
      KPTRS = 2 (transmitted in every 2nd RB)
      LPTRS = 1 (transmitted in each OFDM symbol)
Results
  Practical channel estimation simulation results are provided for next Feb. meeting

## Slide 6: Simulation Assumptions
TBS for DL-DMRS-add-pos = 2 w/o DMRS and data FDM
Note 1: without PT-RS;
Note 2: with PT-RS.
Parameters | Set 1 | Set 2 | Set 3 (Note 1) | Set 3 (Note 2)
CBW(MHz) | 10 | 50 | 50 | 50
SCS(kHz) | 15 | 30 | 60 | 60
RB | 52 | 133 | 66 | 66
Modulation order | QPSK | QPSK | QPSK | QPSK
MCS | MCS4 | MCS4 | MCS4 | MCS4
CFI | 2 | 2 | 2 | 2
Num of DMRS | 3 | 3 | 3 | 3
Channel bits | 11232 | 28728 | 14256 | 13662
TBS (A) | 3368 | 8712 | 4224 | 4224
CRC for TB (A>3824, 24; otherwise 16) | 16 | 24 | 24 | 24
B = A+CRC | 3384 | 8736 | 4248 | 4248
C (Num of CB) | 1 | 2 | 1 | 1
B' (B' = B+C*L) | 3384 | 8784 | 4248 | 4248
Effective code rate | 0.3013 | 0.3058 | 0.2980 | 0.3109
Base Graph Type | BG2 | BG1 | BG1 | BG1

## Slide 7: Impairments
Only the impairments from baseband are considered
  FR1: [2.5]dB
  FR2: TBD
Companies are encouraged to bring more inputs in next meeting for impairments from baseband point of view.