## Slide 1: WF on Clarification of UE Measurement Mode
MediaTek
R4-1801087
Document for: Approval
3GPP TSG-RAN WG4 AH1801
San Diego, US, January 22nd - January 26th, 2018
Agenda item: 4.6.4.1

## Slide 2: Background
If UE is capable to per-FR-gap, it is capable to operate in both measurement modes.
  Per-UE-gap mode
  Per-FR-gap mode
Scenario 1: In NSA, for UE capable to per-FR gap without FR2 serving cells but with both FR1/LTE and FR2 measurement objects, there is an ambiguity on which mode to follow if network configures only one measurement gap pattern ID within #0 to #11.
  Note: an MGRP is still needed to provide a reference for UE to meet the requirement for measurements in FR2, although there is no FR2 serving cell
Scenario 2: For UE capable to per-FR gap with both FR1 and FR2 serving cells and with both FR1/LTE and FR2 measurement objects, there is an ambiguity on which mode to follow if network configures only one measurement gap.

## Slide 3: Scenario 1
In NSA, for UE capable to per-FR gap without FR2 serving cells but with both FR1/LTE and FR2 measurement objects,
  Option 1-1:
    When network configures only the FR1 gap, UE fallbacks to per-UE-gap mode.
  Option 1-2:
    When network configures only the FR1 gap, UE meets requirements corresponding to an effective MGRP X ms toward FR2 measurement objects.
      X is FFS, e.g., fix a value in spec or follow the MGRP of FR1 gap pattern or follow the SMTC period of the FR2 measurement objects.
Clarification is needed to both UE and network sides.
Option 1-2 is adopted due to shorter measurement delay and no additional signaling needed.
The effective MGRP X can be further discussed together with the behavior of UE capable for gap-less measurement.

## Slide 4: Scenario 2
For UE capable to per-FR gap with both FR1 and FR2 serving cells and with both FR1/LTE and FR2 measurement objects,
  When network configures only one gap, companies are encouraged to provide views on UE behavior and the detail requirements in the next meeting.
  Note that related RAN2 decision may also need to be considered