## Slide 1: Way forward on UE behavior during measurement outside measurement gap
NTT DOCOMO
R4-1801088
Document for: Approval
3GPP TSG-RAN WG4 NR-AH#4
San Diego, US, January 22nd - January 26th, 2018
Agenda item: 4.6.4.2

## Slide 2: Updated proposal
Within a SMTC window which is not overlapped with measurement gap in non-CA case:
In FR1 intra-frequency SS-RSRP/RSRQ/SINR measurement:
  For UE not supporting mixed numerology scenarios, UE is not expected to transmit PUCCH/PUSCH or receive PDCCH/PDSCH on SSB symbols to be measured, [1] symbol before each consecutive SSB symbols and [1] symbol after each consecutive SSB symbols within SMTC window duration if useServingCellTimingForSync is enabled
  For UE not supporting mixed numerology scenarios, UE is not expected to transmit PUCCH/PUSCH or receive PDCCH/PDSCH on all symbols within SMTC window duration if useServingCellTimingForSync is not enabled
In FR2 intra-frequency SS-RSRP/SINR measurement:
  UE is not expected to transmit PUCCH/PUSCH or receive PDCCH/PDSCH on SSB symbols to be measured, X symbol(s) before each consecutive SSB symbols and X symbol(s) after each consecutive SSB symbols within SMTC window duration (assuming that useServingCellTimingForSync is always enabled for FR2)
In FR2 intra-frequency SS-RSRQ measurement:
  UE is not expected to transmit PUCCH/PUSCH or receive PDCCH/PDSCH on SSB symbols to be measured , RSSI measurement symbols, X symbol(s) before each consecutive SSB/RSSI symbols and X symbol(s) after each consecutive SSB/RSSI symbols within SMTC window duration (assuming that useServingCellTimingForSync is always enabled for FR2)
Note: whether or not to define specific behavior for rate matching around above symbols is up to RAN1
Note: RAN4 needs to check if cell synchronization accuracy complies with cell phase synchronization requirement in TS 38.133 when useServingCellTimingForSync is enabled
Regarding the value of “X”,
  Option 1: X = [1]
  Option 2: Companies are encouraged to investigate the value of X. If it is identified that X needs to be large value e.g., more than 4, following alternative solutions should be considered
    SMTC-based solution, i.e., all symbols within SMTC window are not available for data transmission/reception
    SSB-slot-based solution, i.e., all symbols within slot(s) containing SSB are not available for data transmission/reception

## Slide 3: Updated proposal
Within a SMTC window which is not overlapped with measurement gap in CA case:
In FR1 intra-frequency SS-RSRP/RSRQ/SINR measurement for intra-band CA without UE capability on simultaneous reception of SSB and data with mixed numerologies,
  in each serving cell, UE is not expected to transmit PUCCH/PUSCH or receive PDCCH/PDSCH on SSB symbols to be measured, [1] symbol(s) before each consecutive SSB symbols and [1] symbol(s) after each consecutive SSB symbols for any one of intra-frequency measurements if the SSB to be measured has different SCS from that for serving cell data and useServingCellTimingForSync is enabled
  in each serving cell, UE is not expected to transmit PUCCH/PUSCH or receive PDCCH/PDSCH on all symbols within SMTC window duration for any one of intra-frequency measurements if the SSB to be measured has different SCS from that for serving cell data and useServingCellTimingForSync is not enabled
In FR2 intra-frequency SS-RSRP/SINR measurement for intra-band CA,
  in each serving cell, UE is not expected to transmit PUCCH/PUSCH or receive PDCCH/PDSCH on SSB symbols to be measured, X symbol(s) before each consecutive SSB symbols and X symbol(s) after each consecutive SSB symbols for any one of intra-frequency measurements
In FR2 intra-frequency SS-RSRQ measurement for intra-band CA,
  in each serving cell, UE is not expected to transmit PUCCH/PUSCH or receive PDCCH/PDSCH on SSB symbols to be measured , RSSI measurement symbols, X symbol(s) before each consecutive SSB/RSSI symbols and X symbol(s) after each consecutive SSB/RSSI symbols within SMTC window duration for any one of intra-frequency measurements (assuming that useServingCellTimingForSync is always enabled for FR2)

## Slide 4: Updated proposal
NR supports to configure enabling/disabling intra-frequency measurement on each NR SCell
  When there is at least one serving cell with intra-frequency measurement within serving cells for intra-band CA, disabling intra-frequency measurement on other serving cell(s) is possible
    FFS: whether additional condition(s) for disabling intra-frequency measurement on NR Scell is/are defined or not
  Detailed signaling design is up to RAN2