## Slide 1: WF on mmW MPR
Qualcomm
3GPP TSG-RAN WG4 AH1801 Meeting
San Diego, CA, January 22 -26, 2018
Agenda: 4.3.2.3.2
R4-1801112

## Slide 2: Background
Previously FR2 MPR was shown to be BW agnostic.
  Several companies have provided simulations [1] [2] [3]
  Previous simulations did not reflect the wide band nature of FR2 architecture.
For narrow BW CC (BW = 50M, 100M), we show that MPR is also for the most part independent of RB allocation [1]
However, large BW (200M, 400M) require more MPR for RB allocations that overlap the region towards edge of CC [4] based on actual measurement
This WF outlines a method and criteria for proposing FR2 MPR due to wide CC BW.

## Slide 3: WF Proposal
Purpose is to layout the framework for FR2 MPR.
A single MPR table is defined for all UEs whether they support the PA calibration gap or not;
  NOTE: whether the PA calibration gap is introduced is addressed in a separate WF
Given:
  Simulation/Measurement Assumptions and Criteria for 50M, 100M CC
  100MHz/60K QPSK DFT-S-OFDM (128RB to allow IBE measurement; 132RB is full allocation) [1] [6]
  Simulation Assumptions for EVM, SEM, ACLR are outlined in [6]
For 200M, 400M, assign MPR based on the following RB boundary conditions as in diagram and table on next slides.
  Test cases should be measured using RB config examples provided
  or
  Comprehensive simulations can be done with the provision to account for frequency variation for various stages in the RF architecture.
Companies are encouraged to measure the effect of MPR required for RB allocations that overlap specific RB boundaries for wide BW CC’s with the example test cases are provided.

## Slide 4: WF Proposal
Shown below is the Proposed Diagram on how MPR is specified according to the RB boundaries for 120K SCS for example
Low BW CC MPR for specified waveform and modulation has MPR = Xn dB, where n =1...8 for the different waveform and modulation.
For larger BW, depending on where RB allocation falls in CC, MPR = Xn + Y1 dB or Xn + Y2 dB as shown.
Y1 and Y2 levels and [RB] boundary points can be fine tuned later, but it is important to at least have infrastruture in place.

## Slide 5: WF Proposal
Proposed Table showing how to specify FR2 power class MPR for different BW and SCS
Only show 60K, 120K SCS, but 240KHz SCS can be added as a 3rd row, if required.
Modulation | MPR (dB) |  |  |  |  | 
 | 50M/100MHz | 200MHz |  | 400MHz |  | 
 | 60K SCS | [63]<RBstart & RBend<[200] | 0=<RBstart=<[63], LCRB>0 or [200]=<RBend=<263, LCRB>0 |  |  | 
 | 120K SCS | [31]<RBstart & RBend<[100] | 0=<RBstart=<[31], LCRB>0 or [100]=<RBend=<131, LCRB>0 | [97]<RBstart & RBend<[166] | [65]<RBstart=<[97] & RBend<[198] or [166]=<RBend<[198] & Rbstart>[65] | 0=<RBstart=<[65], LCRB >0 or [198]=<RBend=<263, LCRB>0
DFT-s-OFDM-Shaped pi/2 BPSK | ≤ X1 | ≤ X1 | ≤ X1 + Y1 | ≤ X1 | ≤ X1 + Y1 | ≤ X1 + Y2
DFT-s-OFDM-pi/2 BPSK | ≤ X2 | ≤ X2 | ≤ X2 + Y1 | ≤ X2 | ≤ X2 + Y1 | ≤ X2 + Y2
DFT-s-OFDM-QPSK | ≤ X3 | ≤ X3 | ≤ X3 + Y1 | ≤ X3 | ≤ X3 + Y1 | ≤ X3 + Y2
DFT-s-OFDM-16 QAM | ≤ X4 | ≤ X4 | ≤ X4 + Y1 | ≤ X4 | ≤ X4 + Y1 | ≤ X4 + Y2
CP OFDM-QPSK | ≤ X5 | ≤ X5 | ≤ X5 + Y1 | ≤ X5 | ≤ X5 + Y1 | ≤ X5 + Y2
CP OFDM-16 QAM | ≤ X6 | ≤ X6 | ≤ X6 + Y1 | ≤ X6 | ≤ X6 + Y1 | ≤ X6 + Y2
DFT-s-OFDM-64 QAM | ≤ X7 | ≤ X7 | ≤ X7+ Y1 | ≤ X7 | ≤ X7+ Y1 | ≤ X7+ Y1
CP OFDM-64 QAM | ≤ X8 | ≤ X8 | ≤ X8 + Y1 | ≤ X8 | ≤ X8 + Y1 | ≤ X8 + Y1

## Slide 6: Example Test Cases
Below are representative test cases.
There are other smaller allocation test cases not shown that can also be tested to determine Y1 and Y2 deltas.
Xn (n=1..8) MPR values are the band agnostic values determined by simulation/measurement.
Waveform | Modulation | MPR, Xn, dB |  |  | BW (MHz) | SCS (KHz) | RBstart | RBend | MPR, dB
DFT-s-OFMD | shaped pi/2 BPSK | X1 |  |  | 50 | 60/120 | any | any | Xn
DFT-s-OFMD | pi/2 BPSK | X2 |  |  | 100 | 60/120 | any | any | Xn
DFT-s-OFMD | QPSK | X3 |  |  | 200 | 60 | 0 | 263 | Xn+Y1
DFT-s-OFMD | 16QAM | X4 |  |  | 200 | 60 | 64 | 199 | Xn
CP-OFDM | QPSK | X5 |  |  | 200 | 120 | 0 | 131 | Xn+Y1
CP-OFDM | 16QAM | X6 |  |  | 200 | 120 | 32 | 99 | Xn
DFT-s-OFMD | 64QAM | X7 |  |  | 400 | 120 | 0 | 263 | Xn+Y2
CP-OFDM | 64QAM | X8 |  |  | 400 | 120 | 32 | 231 | Xn+Y1
 |  |  |  |  | 400 | 120 | 98 | 165 | Xn

## Slide 7: References
[1] R4-1711517 ‘mmW MPR’, Qualcomm, Incorporated, 3GPP TSG-RAN WG4 Meeting #84Bis, Dubrovnik, Croatia, 9-13 September 2017
[2] R4-1712330, ‘MPR Simulation Results for FR2’, Intel Corporation, 3GPP TSG-RAN WG4 Meeting #85, Reno, USA, 27 November - 1 December 2017
[3] R4-1712265, ‘Discussion on NR FR2 MPR’, Samsung, 3GPP TSG-RAN WG4 Meeting #85, Reno, USA, 27 November - 1 December 2017
[4] R4-1801091, “mmW MPR”, Qualcomm, 3GPP TSG-RAN WG4 Meeting AH#1801, San Diego, CA, 22 – 26 January 2018
[5] R4-1711570, “WF on UE IBE for mmWave for MPR evaluation for NR”, Qualcomm
[6] R4-1800150, “MPR evaluation results for FR2”, Intel, 3GPP TSG-RAN WG4 Meeting AH#1801, San Diego, CA, 22 – 26 January 2018