## Slide 1: Power Sharing for FR1 EN-DC
InterDigital

## Slide 2: Background
RAN Plenary agreed in December the WF in RP-172833. This WF confirms two types of UEs supporting NSA is FR1.
  Type 1 - capable of dynamic power sharing P_LTE+P_NR>Pcmax
  Type 2 – not capable of power sharing – works always under Pcmax level through configuration P_LTE+P_NR<=Pcmax or in a TDM mode (single uplink) when P_LTE+P_NR>Pcmax

## Slide 3: RAN 1 – AH-1801 – agreements for EN-DC power sharing (RAN1 meeting minutes)
P_LTE and P_NR are configured separately via UE specific RRC (i.e., as dBm numbers with similar value range as p-Max in LTE)
o P_LTE and P_NR are UE-specific
P_cmax for LTE and P_cmax for NR are derived based on P_LTE and/or P_NR (details to be decided by RAN4)
RAN4 to define maximum total LTE and NR power in FR1 (X_total) that the UE should never exceed.
When dynamic power sharing is used,
o If total power for LTE and NR in FR1 exceeds X_total, UE reduces NR transmission power or drops NR transmission so that total power does not exceed X_total
§ Note: As per previous agreement LTE power control procedure is not changed

## Slide 4: Current concrete proposals for 38.101-3 –AH1801
Qualcomm
  R4-1800398
LGE & InterDigital
  R4-1800519
  R4-1800264 TP for 38.817-01

## Slide 5: Other issues to discuss for EN-DC power sharing in AH-1801
Nokia:
R4-1800068 UE Dynamic power sharing for LTE-NR Dual Connectivity
Huawei:
R4-1800422 on NR EN-DC dynamic power sharing
KDDI:
R4-1800216 Proposals on UE dynamic EN-DC power sharing
Note: the essential issues raised by the above Tdocs have been resolved by the new RAN1 agreement presented in Side 3.

## Slide 6: P_LTE, P_NR signaling impact on RAN4 specs and WF
RAN1 agreement: “P_cmax for LTE and P_cmax for NR are derived based on P_LTE and/or P_NR (details to be decided by RAN4)”
The following impact is foreseen:
P_LTE has to be introduced in the 36.101 specification sub-clause 6.2.5 in the Pcmax equations for single carrier case for the time being.
P_NR has to be introduced in 38.101-1 in the Pcmax equations for single carrier as well.
Way Forward: Companies are asked to provide CRs for next meeting.

## Slide 7: Way Forward for Pcmax TP for 38.101-3
For next meeting:
  The TPs from Qualcomm, Interdigital/LGE to be merged since both proposals have technical merits (to be submitted for next meeting in February).