## Slide 1: WF on network performance analysis for spherical coverage
Samsung
R4-1801118
3GPP TSG-RAN WG4 AH Meeting
San Diego, USA, Jan 22 – 26, 2018
Agenda: 4.3.2.1.5

## Slide 2: Agreements on NW simulation scenarios (with typo correction in the chairman’s notes, in red)
At least indoor hotspots scenario as described in TR 38.803 should be simulated.
For dense urban scenario, use the scenario as described in TR 38.803
For urban macro scenario, use the scenario as described in TR 38.803 (ISD=200m) with 0% indoor as the baseline.
  Companies are encouraged to provide simulation results for ISD of 500m for informative purpose. This does not mean the result of ISD of 500m is not used for the final requirement for spherical coverage.

## Slide 3: Agreements on NW simulation assumptions
UE elevation distribution is modified to be uniform from 0 to 180 degrees.
For UE resource allocation (UL), assume:
  20MHz for outage evaluation
  200MHz for mean throughput evaluation
    FFS how to exclude cell edge UEs in outage, e.g. 0 throughput UEs are excluded from mean throughput calculation)
  Other details FFS
For indoor/outdoor UE ratios, assume:
  For urban macro: 0% is the baseline, 20%, 100% indoor
  For dense urban: 0% is the baseline, 20%, 100% indoor
  Note 1: this is only for initial simulation comparison and NOT for performance requirement conclusion. Further down selection on the ratio to be done for performance requirement conclusion
  Note 2: Results for 20 and 100% are informative.

## Slide 4: Offline agreement on UE UL resource allocation
For UE resource allocation (UL), assume:
  20MHz for outage evaluation
    Option 1: It is assumed that all UEs in the network are allocated fully overlapping resources
    Option 2: Random resource allocation
  200MHz for mean throughput evaluation
    Zero throughput UEs are excluded from the mean throughput calculation

## Slide 5: Offline agreement on blockage modeling
No body blockage and hand grip modelling as baseline.
Companies are encouraged to provide results with blockage
  Study of blockage model is out of scope from the work plan. Companies can still bring results with any model of choice
For information only:
  Why blockage modeling is needed:
    Spherical coverage analysis needs account for realistic blockage due to hand and/or body obstructions
  Why blockage modeling is not needed:
    It should be left to UE designer to mitigate the effect of blockage e.g. with multi-panel diversity, such that there is at least one panel that is not blocked. Hence, from RAN4 requirement point of view, the assumption of no blockage is sufficient
  Remaining time in WI may not allow sufficient time to arrive at an agreeable model

## Slide 6: Offline agreement on UE antenna pattern modeling
For UE antenna pattern modeling (that parameterizes (percentile, EIRP) the spherical coverage requirements), consider the following options:
  Option 1: Use 38.803 UE 2x2 antenna configuration with implementation loss
    To simulate implementation loss, apply a spatial weighting function (in azimuth and elevation) such that the resulting EIRP CDF closely approximates the proposed EIRP CDF (see R4-1800285)
      The spatial weighting function can be provided to facilitate comparison of different EIRP CDF proposals
  Option 2: Up to each company. Companies do not need to disclose the UE antenna pattern assumed in simulation but need to provide the resulting EIRP CDF
For information only
  Back-to-back panels as defined in TR38.803 is assumed in simulation regardless of the underlying number of panels corresponding to the proposed EIRP CDF
  The mask M(𝜑, 𝜃) is applied to the back-to-back panels such that B(𝜑, 𝜃).M(𝜑, 𝜃).A(𝜑, 𝜃) approximates the proposed EIRP CDF, where B(𝜑, 𝜃) is the beamforming gain and A(𝜑, 𝜃) is the antenna element gain
  The gain in the semi-sphere opposite to the boresight direction is modelled by the mask M(𝜑, 𝜃), hence the flat -20dB gain as proposed in R4-1800861 is not necessary (flat gain is just a special case for a particular mask)
  Further study seems still needed to assess Option 1

## Slide 7: Offline agreement on target UL SNR
Target UL SNR = 22dB
Note that the UL PC formula in TR38.803 should be modified to adjust for the conducted/TRP level assumed (see R4-167751)