## Slide 1: WF on DC_42A_n79A
NTT DOCOMO, INC.
3GPP TSG-RAN WG4 Meeting AH-1801
San Diego, USA, 22 – 26 January 2018
R4-1801120

## Slide 2: Background
RAN4#85 in Reno
  It was approved that “DTIB and DRIB should be zero for DC_42A_n79A assuming separate antenna architecture and no MSD should be specified” in Reno [1].
RAN4 AH-1801 in San Diego
  There were comments that most UEs supporting both B42 and n77 have a filter covering 3.3-4.2 GHz only.
  Then, assuming async DC_42_n79 for the UE, it is expected that sufficient isolation between B42 and n79 cannot be achieved in spite of 800 MHz gap. Also, if there is a blocker in the middle of B42 and n79, sensitivity degradation so called half duplex interference may happen.
n77
n79
B42
3.3
3.4
3.6
4.2
4.4
5.0
Synchronization assumed
[1] R4-1712818, “TP for TR 37.863-01-01 DC including LTE Band 42” by Docomo

## Slide 3: Background
In this case, there are several options below for DC_42_n79
Option | Pros | Cons
1) Synchronization (both SF boundary and TX/RX timing) between B42 and n79 i.e. No simultaneous TX/RX | No interference b/w B42 and n79 | Same TDD configuration is forced in B42 and n79
2) Dedicated RF paths for B42 and n77 (how to indicate in the spec?) | Interference b/w B42 and n79 mitigated even without synchronization | HW complexity
3) Specify MSD in B42 and n79 due to frequency proximity (1UL) | No synchronization between B42 and n79 needed | DL performance degraded in both bands
4) Other approach (interference mitigation without synchronization is appreciated) |  | 

## Slide 4: Way forward
Companies are encouraged to provide expected MSD caused by frequency proximity (1UL) for DC_42_n79 in the next meeting.
  Which option is taken will be decided based on the outcome in RAN4#86
Note that below MSD by IMD in LTE band x for 3DL/2UL DC_x-42_n79 is separate discussion from the above. (any option doesn’t exclude the 2UL)
Therefore, it is also requested to provide MSD caused by IMD (2UL) of B42+n79 based on [2] in the next meeting.
n79
B42
x
x
IMD
[2] R4-1800262 “MSD for 3DL/2UL DC_1A-42A_n79A, 3A-42A_n79A and 19A-42A_n79A” Docomo