## Slide 1: WF on 41A_n41A A-MPR Evaluation
Skyworks, […..]
3GPP TSG-RAN WG4 Meeting AH-1801
San Diego, US, 22 - 26 Jan, 2018
R4-1801124

## Slide 2: Background
In Reno meeting it was agreed that requirement will be developed for DC_41A_n41 for a number of cases:
  PC2 and PC3 operation
  1 transmit and two transmit path
It was also agreed that equal PSD is a realistic power sharing scenario for collocated LTE/NR BS
In this meeting a number of papers discussed the assumptions and conditions to be applied to derive NS04 A-MPR:
  How to apply the 2 separate SEM masks?
  How to model the two PA case, assumptions on antenna isolation?
  What Power sharing should be assumed?
  How is A-MPR applied?

## Slide 3: Complexity of evaluation
To derive A-MPR for NS04 the number of variables is large:
  Need to be tested against two SEM masks and two emission levels as well as the -30dBm emissions limit
  A large number of NR channel bandwidths and SCS
  A few LTE channel bandwidths
  A number of LTE to NR channel gaps
  For all possible RB allocations
  The power needs to be swept
There is thus a need to reduce the cases at least for first alignments and understanding what are the critical cases.

## Slide 4: Reverse IMD aspect
One aspect is that in the 2 PA case there is a reverse component from antenna coupling and a forward component from PCB leakage
It was shown by measurements that the IMD is dominated by the reverse component and thus the leakage path can be ignored.
Modeling of reverse IMD only in PA should be tried by deriving an equivalent input interference level in a forward IMD PA model including the model verification against measurements

## Slide 5: Power sharing, allocation
Most likely power sharing will not always result in an equal PSD situation equal power is expected to be the worst
For first simulations the amount of cases to be evaluated needs to be limited using e.g. only smallest (1RB), largest and a medium allocation and their permutations should be
Also the lowest SCS case is the worst case (higher PSD, more allocations, higher SU) and could be used

## Slide 6: SEM mask
During the meeting it was the common understanding that when the LTE and NR SEM masks overlap the most relaxed limit is used
The -30dBm/MHz general emission limit should also be verified

## Slide 7: WF proposal
For first step A-MPR evaluation the following simplifications are agreed to identify critical IMD cases:
  To reveal critical IMD cases equal power is used
  Only one CC LTE and NR to start with permutation of CCs
  LTE and NR RB allocation split proportional to respective channel bandwidths and 1RB LTE and 1RB NR should be included, at least smallest, a medium and the largest allocations and their permutations should be evaluated
  Only lowest SCS is used for NR
  Start with 1PA PC3 case to identify critical cases that can then be used for the other cases (2PA and PC2)
  Only reverse path is evaluated for the 2 PA case
  Respective LTE and NR TRX impairments are used
This first pass will allow to identify problematic cases for refined evaluation

## Slide 8: WF: Open points for A-MPR
Use of equal power or equal PSD power sharing as worst case for emissions needs to be understood
How each RAT MPR/A-MPR should be applied first to each carrier needs to be considered
A-MPR could be applied by reducing both carriers equally or NR side only
Single switched UL may be used alternatively if significant A-MPR is found
Validity of reverse IMD modeling should be verified by measurements
Critical cases need to be verified by measurements given the large bandwidth involved for the single PA scenario
Companies are encouraged to provide input on the open points above

## Slide 9: References
[1] R4-1712448, Band n41 A-MPR, Nokia, Nokia Shanghai Bell, Skyworks Solutions, Inc., RAN4#85
[2] R4-1800984, Simulating single PA and dual PA architectures for DC_41A-n41A, Qualcomm Incorporated, RAN4#AH-1801
[3] R4-1800983, Discussion on SEM requirements for DC_41A-n41A, Qualcomm Incorporated, RAN4#AH-1801
[4] R4-1800553, DC_41A_n41A A-MPR measurements, Skyworks Solutions Inc., RAN4#AH-1801