## Slide 1: WF on CDF based EIS requirements exception case for NR UE at mmWave
LG Electronics, MediaTek
3GPP TSG-RAN WG4 Meeting AH-1801 San Diego, California, USA, 22 - 26 January 2018 Agenda Item: 4.3.3.1.3
R4-1801138

## Slide 2: Background
Peak EIS requirement at FR2 has been discussed and will be defined in TS38.101-2.
One remaining EIS requirements is whether to define the CDF based EIS requirements or not.
The CDF based EIS for spherical coverage is quite similar to that with EIRP if the beam reciprocity between Rx beam and Tx beam is guaranteed.
During online/offline discussions, companies discussed whether the beam correspondence is optional feature or not. Concerns are if the beam correspondence requirements are not tested, CDF based EIS requirements should be needed.
RAN4 already discussed to define beam correspondence RF requirements and it will be defined in TS38.101-2 regardless of mandatory/optional test.
This WF is on the related discussions on how to address CDF based EIS spherical coverage.

## Slide 3: Way Forward
The CDF based EIS spherical coverage requirement in FR2 will be covered by CDF based EIRP requirements if the UE fulfills beam correspondence RF requirements.
  If UE indicates the beam correspondence capability, then the CDF based EIS requirements do not need to be tested.
  If UE indicates no beam correspondence capability, then the CDF based EIS requirements shall be tested.
RAN4 will specify the beam correspondence RF requirements
  Detailed test methodology will be discussed based on proposed papers