## Slide 1: WF on NR intra-band contiguous CA
NTT DOCOMO, INC.
3GPP TSG-RAN WG4 Meeting AH-1801
San Diego, USA, 22 – 26 January 2018
R4-1801183

## Slide 2: Background
The latest NR WID lists below intra-band contiguous NR CA [1]
While it was agreed to specify 8x100, 4x200 and 2x400 MHz for n257 in Rel-15 [2], other BW combinations are still FFS
Combination | contact name, company | other supporting companies (min. 3)
n77 contiguous | Naoto Iizasa NTT DOCOMO | Nokia, NEC, Fujitsu
n78 contiguous | Naoto Iizasa NTT DOCOMO | Nokia, NEC, Fujitsu, SK telecom
n79 contiguous | Naoto Iizasa NTT DOCOMO | Nokia, NEC, Fujitsu
n257 Contiguous | Ilwhan Kim KT | Samsung ,LG electronics, Intel

## Slide 3: Way forward
The BW combinations below to be specified for “2CC” cases
  In order to reduce number of BW combinations, each aggregated BW can only have one BW combination and with symmetric BW if possible
    Ex1) For aggregated BW of 120 MHz, only 60+60 MHz is specified
    Ex2) For aggregated BW of 140 MHz, either 60+80 or 40+100 MHz is specified
  “2CC” doesn’t necessarily mean CA bandwidth Class C
  The notation is FFS in other papers
BW combinations > 2CC to be discussed in the next meeting.
Component carriers in order of increasing carrier frequency |  |  | 
NR band | Channel bandwidths for carrier [MHz] | Channel bandwidths for carrier [MHz] | Maximum aggregated bandwidth [MHz]
Band n77 Band n78 Band n79 | 60 | 60 | 200
 | 60, 80 | 80 | 
 | 50, 80, 100 | 100 | 
Band n257 | 50, 100 | 100, 200, 400 | 800
 | 200 | 200, 400 | 
 | 400 | 400 | 

## Slide 4: Way forward
UE RF requirements consisting of the same aggregated BW to be identical regardless of number of CCs
  Ex) SEM of 8x100, 4x200 and 2x400 MHz will be identical

## Slide 5: References
[1] RP-172834, Revised WID on New Radio Access Technology, NTT DOCOMO, INC.
[2] R4-1800783, Discussion on CA configuration for intra-band NR CA in mmW NTT DOCOMO, INC.