## Slide 1: WF on network performance analysis for spherical coverage
Samsung, Qualcomm Incorporated, Apple, Huawei, LGE, Telecom Italia, Verizon, OPPO, Vodafone
R4-1801187
3GPP TSG-RAN WG4 AH Meeting
San Diego, USA, Jan 22 – 26, 2018
Agenda: 4.3.2.1.5

## Slide 2: Agreements on NW simulation scenarios
At least indoor hotspots scenario as described in TR 38.803 should be simulated.
For dense urban scenario, use the scenario as described in TR 38.803.
For urban macro scenario, use the scenario as described in TR 38.803 (ISD=200m, 400m) with 0% indoor as the baseline.

## Slide 3: Agreements on NW simulation assumptions
UE elevation distribution is modified to be uniform from 0 to 180 degrees.
For UE resource allocation (UL), assume:
  20MHz for outage evaluation
    Option 1: It is assumed that all UEs in the network are allocated fully overlapping resources
    Option 2: Random resource allocation
  200MHz for mean throughput evaluation
    Zero throughput UEs are excluded from the mean throughput calculation
For indoor/outdoor UE ratios, assume:
  For urban macro: 0% is the baseline, 20%, 100% indoor
  For dense urban: 0% is the baseline, 20%, 100% indoor
  Note 1: this is only for initial simulation comparison and NOT for performance requirement conclusion. Further down selection on the ratio to be done for performance requirement conclusion
  Note 2: Results for 20 and 100% are informative.

## Slide 4: Agreement on blockage modeling
No body blockage and hand grip modelling as baseline.
Companies are encouraged to provide results with blockage.
  Study of blockage model is out of scope from the work plan. Companies can still bring results with any model of choice.

## Slide 5: Agreement on target UL SNR
Target UL SNR = 22dB.
Note that the UL PC formula in TR38.803 should be modified to adjust for the conducted/TRP level assumed (see R4-167751).

## Slide 6: WF on UE antenna pattern modeling
For UE antenna pattern modeling (that parameterizes (percentile, EIRP) the spherical coverage requirements), consider the following options:
  Option 1: based on mathematical modelling. A detailed explanation of the model including each step in the simulation process and the corresponding simulated CDF should be provided
  Option 2: based on measured or simulated pattern. The assumption(s) used from the next slide and the corresponding EIRP CDF should be provided

## Slide 7: Assumptions for EIRP CDF
Assumptions that has been agreed in RAN4#85
This table can be further updated subject to any further agreements
 |  | Assumptions1 | Assumptions2 | Assumptions3 | Assumptions4 | Assumptions5 | Assumptions6 | Notes
Frequency range |  | n257 | n257 | n257 | n257 | n257 | n257 | 
# of antenna in an antenna module/set (# of patches, # of dipoles, etc.) |  | - | - | - | - | - | - | Depends on the current implementation
# of antenna module/set in total |  | 1 | 1 | 2 | 2 | 3 | 3 | 
Finite UV test points |  |  |  |  |  |  |  | Finite test point shall be the baseline
Beam phase shifter controller | degree | 45 | 45 | 45 | 45 | 45 | 45 | Finite beam shall be the baseline
Antenna type (patch, dipole, or both) |  | - | - | - | - | - | - | Depends on the current implementation
Antenna module/set location (front, back, top-side, left-side, right-side, bottom-side) |  | Top / Bottom | Top / Bottom | Top & Bottom | Top & Bottom | Left & Right & Bottom | Left & Right & Bottom | combination of the lists are not precluded.
Front cover (Plastic, Glass, Ceramic, Metal) |  | Glass | Glass | Glass | Glass | Glass | Plastic | 
Back cover (Plastic, Glass, Ceramic, Metal) |  | Glass | Glass | Glass | Glass | Glass | Plastic | 
Side cover / Frame (Plastic, Glass, Ceramic, Metal) |  | Metal | Plastic | Metal | Metal | Metal | Plastic | Legacy antenna performance degradation by mutual coupling w/ NR antenna or vice versa.
Device size (WxHxD) | cm3 | 66.6 | 66.6 | 66.6 | 66.6 | 66.6 | 66.6 | This is for information
Display panel – Full (Y) or Partial (N) | Y/N | Y | Y | Y | N | Y | Y | 
Bezel Margin | mm | 1.5 | 1.5 | 1.5 | 1.5 | 1.5 | 1.5 | Module can’t be placed outer edge of UE to secure mechanical reliability