## Slide 1: WF on HPUE definition for NR PC2 UE
CMCC
3GPP TSG-RAN WG4 Meeting AH-1801 R4-1801190
San Diego, USA, 22 – 26 January 2018

## Slide 2: Background
The following NR bands were approved to support PC2 HPUE for 5G NR[1][2]:
Band n41 (2496 – 2690 MHz)
UL-MIMO (2Tx 23+23dBm) and 1Tx 26dBm are supported for NR Band n41
Band n77 (3.3 - 4.2 GHz)
Band n78 (3.3 - 3.8 GHz)
Band n79 (4.4 - 5 GHz)
References
  [1] R4-1706068 WF on high power UE for 3.5GHz CMCC
  [2] R4-1709974 WF on HPUE requirements in Rel15 Huawei, HiSilicon

## Slide 3: Agreements
5G NR PC2 HPUE definition for SA scenario
  UL MIMO (2Tx 23+23dBm) with total output power of 26dBm is supported by specification for NR Bands n77,n78,n79
  1Tx +26dBm HPUE is also considered for PC2 UE for NR Bands n77,n78,n79