## Slide 1: WF on mmW MPR
Qualcomm
3GPP TSG-RAN WG4 AH1801 Meeting
San Diego, CA, January 22 -26, 2018
Agenda: 4.3.2.3.2
R4-1801192

## Slide 2: Background
Previously FR2 MPR was shown to be BW agnostic.
  Several companies have provided simulations [1] [2] [3]
  Previous simulations did not reflect the wide band nature of FR2 architecture.
For narrow BW CC, we show that MPR is also for the most part independent of RB allocation [1]
However, wide BW CC require more MPR for RB allocations that overlap the region towards edge of CC [4] based on actual measurement

## Slide 3: WF Proposal
Goal is to provide a simple method to account for MPR for wider BW’s.
A single MPR table is defined for all UEs whether they support the PA calibration gap or not;
  NOTE: whether the PA calibration gap is introduced is addressed in a separate WF
MPR 0dB waveform is 100MHz/60K QPSK DFT-S-OFDM 128RB0 to allow IBE measurement; 132RB is full allocation) [1] [5]
Simulation Assumptions for EVM, SEM, ACLR are outlined in [6]
For 50M/100M/200M assign a single MPR value relative to MPR 0 for each waveform and modulation.
For 400M, add MPR offset based on practical implementation
  Companies are encouraged to measure the effect large BW on MPR

## Slide 4: WF Proposal
MPR, Xn, [n=1..8] values are relative to MPR 0dB.
Y dB, is the MPR delta due to excess BW.
 |  | MPR | 
Waveform | Modulation | 50M/100M/200M | 400M
DFT-s-OFMD | shaped pi/2 BPSK | <=X1 | <=X1+Y
DFT-s-OFMD | pi/2 BPSK | <=X2 | <=X2+Y
DFT-s-OFMD | QPSK | <=X3 | <=X3+Y
DFT-s-OFMD | 16QAM | <=X4 | <=X4+Y
CP-OFDM | QPSK | <=X5 | <=X5+Y
CP-OFDM | 16QAM | <=X6 | <=X6+Y
DFT-s-OFMD | 64QAM | <=X7 | <=X7+Y
CP-OFDM | 64QAM | <=X8 | <=X8+Y

## Slide 5: References
[1] R4-1711517 ‘mmW MPR’, Qualcomm, Incorporated, 3GPP TSG-RAN WG4 Meeting #84Bis, Dubrovnik, Croatia, 9-13 September 2017
[2] R4-1712330, ‘MPR Simulation Results for FR2’, Intel Corporation, 3GPP TSG-RAN WG4 Meeting #85, Reno, USA, 27 November - 1 December 2017
[3] R4-1712265, ‘Discussion on NR FR2 MPR’, Samsung, 3GPP TSG-RAN WG4 Meeting #85, Reno, USA, 27 November - 1 December 2017
[4] R4-1801091, “mmW MPR”, Qualcomm, 3GPP TSG-RAN WG4 Meeting AH#1801, San Diego, CA, 22 – 26 January 2018
[5] R4-1801107, “On IBE for FR2”, Intel, 3GPP TSG-RAN WG4 Meeting AH#1801, San Diego, CA, 22 – 26 January 2018
[6] R4-1800150, “MPR evaluation results for FR2”, Intel, 3GPP TSG-RAN WG4 Meeting AH#1801, San Diego, CA, 22 – 26 January 2018
On IBE for FR2
On IBE for FR2