## Slide 1: WF on EIRP CDF for spherical coverage
Samsung, MediaTek,…
R4-1801194
3GPP TSG-RAN WG4 Meeting AdHoc-1801
Reno, Nevada, USA, November 27 – December 1, 2017
Agenda: 4.3.2.1.4

## Slide 2
Work plan for Spherical coverage has been agreed in RAN4 #85 [1]
  RAN4 NR AH #4 (January ’18)
    Initial discussion of simulation results (Both EIRP CDF and Network) based on the harmonized assumptions in this way forward.
    Propose harmonized NW model assumptions and update based on preliminary analysis.
  RAN4 #86 (February ’18)
    Deadline to submit the EIRP CDF simulation results based on the harmonized assumptions. Target preliminary EIRP CDF spherical requirement, based on the simulation outcomes.
    Continue to improve the NW simulation accuracy reflecting initial EIRP CDF requirement (from AH #4)
    Initial discussion of measurement results for prototype devices
  RAN4 #86bis (April ’18)
    Continue to improve the NW simulation accuracy reflecting preliminary EIRP CDF requirement (#86)
    Continue to improve the prototype measurement effort and compare to preliminary EIRP CDF simulation
  RAN4 #87 (May ’18)
    Finalize the spherical coverage requirement for handheld UEs based on the contributions
Background

## Slide 3
Proposals for RAN4 AH-1801 (AI 4.3.2.1.3) were as follows,
Inputs to RAN4 AH-1801
Tdoc # [Ref] | Target Assumptions | Display | Side Cover material | Proposals
R4-1800037 [2] | 3, 4 | Partial, Full | Metal, Plastic | Important to understand the achievable performance based on real phone product condition. All screen display and metal bezel would be phone product selling points. (-13.7dB from the peak to 20%-tile EIRP, based on all screen display and metal bezel condition)
R4-1800888 [3] | 3, 4 | Partial, Full | Plastic, Metal (no covering the antenna) | The difference between peak EIRP and the 20%-tile is in the order of 10dB. Measurements on real prototypes is needed to verify the results.
R4-1800369 [4] | N/A | N/A | Plastic, Metal | Cover material and thickness have the most significant effect on radiated performance. Need for UE packaging innovation to minimize packaging loss.
R4-1800990 [5] | 1, 2, 3, 5, 6 | Full | Plastic, Metal | Differences between metal and plastic frame make the EIRP at each point decrease by up to 4dB. The gap is bigger with the lower CDF point.

## Slide 4
As summarized in page 3, all contributions are considering the real-product UE aspect especially on cover material on EIRP CDF discussion
Based on that, it should be the baseline to consider that the restrictions of real product UE to decide the spherical coverage requirement
In order to give a clear information to RAN4#86, companies are encouraged to submit their contribution focusing on following results to meet the workplan in page 2
  Information of display and cover material near antennas should be included
  EIRP CDF Curve or EIRP loss at each %-tile point, [20-50%], from the peak in dB
Other appropriate information are not precluded, i.e., measurement results for prototype devices. See the workplan
Way Forward

## Slide 5
 | Tdoc # | Title | Source
[1] | R4-1714455 | WF on spherical coverage in FR2 | Samsung, Apple, LGE, Intel, Oppo, Xiaomi, Vivo, MediaTek
[2] | R4-1800037 | EIRP CDF Simulation Analysis for Spherical Coverage Topic | MediaTek Inc.
[3] | R4-1800888 | UE Spherical coverage at mmWave 28GHz | Sony, Ericsson
[4] | R4-1800369 | On UE Packaging Loss, Simulation Results | Qualcomm Incorporated
[5] | R4-1800990 | Further efforts on EIRP CDF for spherical coverage | Samsung
References

## Slide 6
Companies are encouraged to submit their contribution in the following templates.
Appendix(1) - Template for the result comparison
Company | - | Company A | Company B | Company C | Company D | Company E | Company F
Display | Partial / Full |  |  |  |  |  | 
Side cover (cover material near antennas) | Metal / Plastic |  |  |  |  |  | 
EIRP @ 100%%-tile point | dBm |  |  |  |  |  | 
EIRP @ 50% | dB |  |  |  |  |  | 
EIRP @ 40% | dB |  |  |  |  |  | 
EIRP @ 30% | dB |  |  |  |  |  | 
EIRP @ 20% | dB |  |  |  |  |  | 

## Slide 7: Appendix(2) – Assumptions for EIRP CDF
Assumptions has been agreed in RAN4#85
 |  | Assumptions1 | Assumptions2 | Assumptions3 | Assumptions4 | Assumptions5 | Assumptions6 | Notes
Frequency range |  | n257 | n257 | n257 | n257 | n257 | n257 | 
# of antenna in an antenna module/set (# of patches, # of dipoles, etc.) |  | - | - | - | - | - | - | Depends on the current implementation
# of antenna module/set in total |  | 1 | 1 | 2 | 2 | 3 | 3 | 
Finite UV test points |  |  |  |  |  |  |  | Finite test point shall be the baseline
Beam phase shifter controller | degree | 45 | 45 | 45 | 45 | 45 | 45 | Finite beam shall be the baseline
Antenna type (patch, dipole, or both) |  | - | - | - | - | - | - | Depends on the current implementation
Antenna module/set location (front, back, top-side, left-side, right-side, bottom-side) |  | Top / Bottom | Top / Bottom | Top & Bottom | Top & Bottom | Left & Right & Bottom | Left & Right & Bottom | combination of the lists are not precluded.
Front cover (Plastic, Glass, Ceramic, Metal) |  | Glass | Glass | Glass | Glass | Glass | Plastic | 
Back cover (Plastic, Glass, Ceramic, Metal) |  | Glass | Glass | Glass | Glass | Glass | Plastic | 
Side cover / Frame (Plastic, Glass, Ceramic, Metal) |  | Metal | Plastic | Metal | Metal | Metal | Plastic | Legacy antenna performance degradation by mutual coupling w/ NR antenna or vice versa.
Device size (WxHxD) | cm3 | 66.6 | 66.6 | 66.6 | 66.6 | 66.6 | 66.6 | This is for information
Display panel – Full (Y) or Partial (N) | Y/N | Y | Y | Y | N | Y | Y | 
Bezel Margin | mm | 1.5 | 1.5 | 1.5 | 1.5 | 1.5 | 1.5 | Module can’t be placed outer edge of UE to secure mechanical reliability

## Slide 8
Gap 2, G2 mm
Antenna substrate, H4 mm, including Ground Plane
Gap 4, G4 mm
Edge Material 1, W1 mm
Display, H1 mm
Edge material 4, H7 mm
Distances from antennas to any material (d1 and d2) must be carefully noted, specially those in the direction of radiation (H6)
Properties needed for simulation are: dielectric constant ɛr and dielectric loss tan δ
  since both parameters are frequency dependent, companies should consider the frequency at which these are reported in spec sheet, or were characterized
Layer Properties |  |  |  | 
Name | Material | Thickness | Ɛr | tan δ
Antenna substrate Dielectrics | TBD | H4 |  | 
Antenna Substrate Metals | copper | - | conductivity | 
Gap 1 | Air/Plastic/? | G1 |  | 
Gap 2 | Air/Plastic/? | G2 |  | 
Gap 3 | Air/Plastic/? | G3 |  | 
Gap 4 | Air/Plastic/? | G4 |  | 
Edge material 1 | Glass/Plastic/Metal | W1 |  | 
Edge material 2 | Glass/Plastic/Metal | W2 |  | 
Edge material 3 | Glass/Plastic/Metal | W3 |  | 
Edge material 4 | Glass/Plastic/Metal | W4 |  | 
Device Cross-Section
Edge Material 2, W2 mm
Edge Material 3, W3 mm
Gap1
G1 mm
Gap 3
G3 mm
Appendix(3) – EIRP CDF simulation environment