## Slide 1: WF on CA BW class
Qualcomm, [ ]
R4-1801197
3GPP TSG-RAN WG4 AH meeting
San Diego, USA, 22 - 26 Jan 2018
Agenda item: 4.1.2.1

## Slide 2: Background
[1] R4-1800065, NR CA BW Class, Nokia
[2] R4-1800073, Views on NR CA channel bandwidth class, ZTE
[3] R4-1800399, CA Bandwidth class definition, Qualcomm
[4] R4-1800718, CA BW classes, discussion paper, Ericsson
[5] Intel

## Slide 3: Background
Two methods were considered
  1) Denoting CA configuration by aggregated BW and maximum number of CCs [3]
    CA_nX(Y,Z) where X is NR band, Y is maximum aggregated BW, Z is maximum number CCs
    Exact CC combinations are signaled as BB capability
    This method will require exact CC BW combinations for specific CA configuration listed somewhere e.g. (YY,YY), (YY,ZZ), … where YY and ZZ are BW of individual CC BWs for this configuration
  2) Denoting traditional approach but with more flexibility [1,4]
Third approach was proposed in [2]

## Slide 4: Observations from discussions
Exact CA configuration must be defined somewhere
  It means every requested CC combination for each band needs to be known by UE and by network explicitly somehow
Three methods could be identified
  A) UE signals explicitly each band and CA configuration
  B) CA configurations are written in to UE requirements (38.101) and UE signals supported CA configurations and version of specification
  C) CA configurations are written in to UE requirements (38.101) and UE signals supported CA configurations and specific identifier which set of CC combinations (existing LTE BCS method)

## Slide 5: Observations on both methods
1 A: increases signaling overhead
1 B: CA configurations release (or spec version) dependent
1 C: introduces BCS concept
Method 2 (traditional) increases amount of signaled CA configurations for one band or band combination
  Similarly to method 1, exact CC combinations must be stated somewhere regardless of CA BW class and same options are available as for method 1
  E.g. if UE supports CA_n78D, then it also may or may not support CA_n78C and B and in addition BCS concept or version reference to spec is needed

## Slide 6: Method different from LTE
Class of CA is defined based on number aggregated CCs
  C = 2 CC
  D = 3 CC
Intra-band contiguous CA:
  Total aggregated BW for each CC combinations will be written to 38.101
  CC BWs combinations for each CA configuration will be written in to 38.101
  Forward compatibility is FFS
    Option 1: UE can refer to version of spec
    Option 2: UE can refer to BCS
  Total maximum aggregated BW will be used to denote intra-band CA support:
    E.g. CA_n78(200)
    Wherther to use number or letter is FFS
    UE will support all CA configurations for that band with lower aggregated BW from same CA BW Class group

## Slide 7: Example intra-band contiguous
If UE declares support CA_n78(160,C)_BCS1 it supports all configurations in yellow
CA Class C |  |  |  | 
CA band | CC1 [MHz] | CC2 [MHz] | Agg. BW | BCS
n78, n77 | 50 | 60 | 110 | 1
 | 50 | 80 | 130 | 
 | 60 | 60 | 120 | 
 | 60 | 80 | 140 | 
 | 80 | 80 | 160 | 
 | 50 | 100 | 150 | 
 | 80 | 100 | 180 | 
 | 100 | 100 | 200 | 
n79 | 50 | 60 | 110 | 1
 | 50 | 100 | 150 | 
 | 80 | 100 | 180 | 
 | 100 | 100 | 200 | 
Example, numbers for information only

## Slide 8: Views on Inter-band and intra-band non-contiguous
Inter-band CA: FFS to study if UE can support all BWs for indicated bands
  BB processing capability may have limitations e.g. up to 160 MHz
  UE could declare support for CA_n78-n79 if maximum aggregated BW is limited to 160 MHz
    E.g. CA_n78(100)-n79(60) means total aggregated is 160 MHz and all BWs lower than 100 and 60 for bands 78 and 79 are supported.
  If all CH BW are mandated, then UE could not support this interband combination at all
Intra-band non-contiguous:
  Will be handled similarly as inter-band from notation perspective
  Maximum span of CCs will be defined as part of CA capability

## Slide 9: Way Forward
Companies are encouraged to study method described in this document
Advantage compared to LTE method should be studied
Companies to confirm if all channel BWs for denoted bands can be supported in inter-band CA
How to capture intra-band non-contiguous with maximum CC separation at least for FR2 should be studied
Information from LS from RAN2 (R4-1801290) and agreement in RP-172832 should be considered