## Slide 1: WF on NR intra-band contiguous CA for n77, n78, n79 and n257
NTT DOCOMO, INC.
3GPP TSG-RAN WG4 Meeting AH-1801
San Diego, USA, 22 – 26 January 2018
R4-1801201

## Slide 2: Background
The latest NR WID lists below intra-band contiguous NR CA [1]
While it was agreed to specify 8x100, 4x200 and 2x400 MHz for n257 in Rel-15 [2], other BW combinations are still FFS
Combination | contact name, company | other supporting companies (min. 3)
n77 contiguous | Naoto Iizasa NTT DOCOMO | Nokia, NEC, Fujitsu
n78 contiguous | Naoto Iizasa NTT DOCOMO | Nokia, NEC, Fujitsu, SK telecom
n79 contiguous | Naoto Iizasa NTT DOCOMO | Nokia, NEC, Fujitsu
n257 Contiguous | Ilwhan Kim KT | Samsung ,LG electronics, Intel

## Slide 3: Way forward
CC1 [MHz] | CC2 [MHz] | Agg. BW
50 | 60 | 110
50 | 80 | 130
60 | 60 | 120
60 | 80 | 140
80 | 80 | 160
50 | 100 | 150
80 | 100 | 180
100 | 100 | 200
FFS in the next meeting
  BW combinations for more than 2CC
  Whether or not to follow the concept of “Component carriers in order of increasing carrier frequency” in 36.101 for NR specs
For Band n77, n78, n79
CC1 [MHz] | CC2 [MHz] | Agg. BW
50 | 100 | 150
50 | 200 | 250
50 | 400 | 450
100 | 100 | 200
100 | 200 | 300
100 | 400 | 500
200 | 200 | 400
200 | 400 | 600
400 | 400 | 800
For Band n257

## Slide 4: Way forward
Baseline
  UE RF requirements consisting of the same aggregated BW to be identical regardless of number of CCs
    Ex) SEM of 8x100, 4x200 and 2x400 MHz will be identical

## Slide 5: References
[1] RP-172834, Revised WID on New Radio Access Technology, NTT DOCOMO, INC.
[2] R4-1800783, Discussion on CA configuration for intra-band NR CA in mmW NTT DOCOMO, INC.