## Slide 1: WF on Channel Raster to RE Mapping
ZTE Corporation
3GPP TSG-RAN WG4-NR Meeting AH # 1801
San Diego, California, USA, 22 – 26 Jan, 2018
R4-1801234

## Slide 2: Background
PRB grid alignment among different SCS configuration is specified in RAN1 specs TS 38.211 (Section 4.4.4.2 and Section 4.4.4.3)
  SC#0 of reference resource block #0 is denoted as “reference point A”
    Obtained from the higher-layer parameters for PCell UL/DL, SCell UL/DL and SUL respectively
    Common for all SC configurations
  For each SCS configuration, common resource blocks are defined, and its SC#0 of RB#0 coincides with “reference point A”
  Furthermore, offset between a reference location and “reference point A” is RRC signaled to a UE expressed based on 15kHz SCS for FR1 and 60kHz SCS for FR2

## Slide 3: Background (Cont’d)
RAN4 specifies channel raster to resource element in TS 38.104 (Section 5.4.2.2)
  In principle channel raster is mapped to the center of transmission bandwidth configuration for a given SCS

## Slide 4: Agreements
Revise texts of Section 5.4.2.2 in TS 38.104 by clarifying that only a single numerology is on the channel raster according to the current channel raster to resource element mapping
  The numerology mapped to the channel raster is termed as “reference numerology”
For mixed numerologies, follow RAN1 specs by referring to the reference numerology

## Slide 5: Way Forward
  Which numerology is chosen as reference numerology:
    Option 1: up to scheduler
      FFS: Whether or not different PRB grid resulting from different reference numerology among adjacent BSs may generate unnecessary adjacent network interference
    Option 2: specifying a default numerology for each CBW
    Other options not precluded
  Companies are encouraged to provide studies on pros and cons for different options

## Slide 6: Reference
R4-1711731, LS on PRB grid in the NR, RAN4
R4-1800005, Reply LS on PRB grid in the NR, RAN1
R4-1800335 PRB alignment for multiple numerologies, ZTE
R4-1800608, Draft CR to TS 38.104: RB alignment with different numerologies (Section 5.3.4), ZTE