## Slide 1: WF on Sync Raster Calculations
Agenda Item: 4.2.2.2
Document for: Approval
Source: Ericsson
3GPP TSG-RAN WG4 AH-1801 Tdoc R4-1801237 San Diego, CA, US, 22 – 26 January, 2018

## Slide 2: Background
The present equations and tables for sync channel raster are based on the agreed WF at RAN4#85 in Reno:
  R4-1714294, "WF on channel raster" (Nokia).
  R4-1714514, "WF on Synchronization Raster" (Qualcomm).
Previous way forward also needs to be considered:
  R4-1708850, “WF on Channel Raster for NR” (Qualcomm Incorporated, Ericsson, Vodafone, AT&T, Sprint, Verizon, ZTE) “Channel raster for Bands above 2.6 GHz (above Band 41) is tentatively agreed to be a subcarrier based raster”

## Slide 3: Agreements for equations in Table 5.4.3.1-1
Modification to equations in Table 5.4.3.1-1:
  Frequency range for the first row is extended to 2700 MHz (This makes it possible to cover also bands n7 and n38, as indicated in the WF in R4-1708850)
  An extra column is added to explain how GSCN are derived
Frequency range | SS block frequency position SSREF | GSCN | Range of GSCN
0 – 2700 MHz | N * 900 kHz + M * [5 kHz] N=1:3000, M=-1:1 | 3N + M - 1 | 1 – 9000
2400 – 24250 MHz | 2400 MHz + N * 1.44 MHz N= 0:15173 | 9001 + N | 9001 – 24174
24250 – 100000 MHz | 24250.08 MHz + N * 17.28 MHz N= 0:4383 | 24175 + N | 24175 – 28558

## Slide 4: Agreements for calculating sync raster points
Selection of GSCN for Table(s) in clause 5.4.3.3:
  Include GSCN that correspond to SS block that completely fit within the channel bandwidth accounting for guard bands
  Guard bands are calculated based on the minimum channel BW, the SCS for the SS block and the corresponding NRB (spectrum utilization), assuming the RF reference frequency at the center of a block
  For step size <N>, GSCN that are multiples of N are selected (this ensures overlapping bands have same GSCN)
The attached spread sheet demonstrates the calculations and resulting GSCN ranges

## Slide 5: Open issues
For GSCN ranges, open issues are:
  n7, n38: Need confirmation from operators that a 100 kHz based channel raster is used (in line with WF)
  n41: Inclusion of 30 kHz SCS in addition to 15 kHz
  n66: Inclusion of GSCN for the SDL ranges
  n70, n75, n76: Inclusion of GSCN for SDL bands
  n79: Conclusion on step size
  n258: Inclusion of 240 kHz SS SCS in addition to 120 kHz
  n257, n260, n258: What NRB to use for 240 kHz SS SCS
In addition, a change of ΔFshift from 5 kHz to a larger number (1st row) may change some GSCN ranges

## Slide 6: Reference input documents
R4-1800215, "Discussion on sync raster" (Samsung).
R4-1800274, "Channel and sync raster alignment for 30 kHz SCS" (Ericsson).
R4-1800297, "Corrections on NR FR1 synchronization raster entries" (MediaTek Inc.).
R4-1800299, "Reconsideration of NR sync raster for 100kHz channel raster" (MediaTek Inc.).
R4-1800432, "Discussion on sync raster for NR FR1" (LG Electronics Inc.).
R4-1800481, "Further discussion on some issues of synchronization raster" (Huawei, HiSilicon).
R4-1800857, "Remaining issues on SS raster" (Nokia, Nokia Shanghai Bell).
R4-1800874, "Examining the mapping of SS blocks to the GSCN" (Huawei Telecommunication India).