## Slide 1: Way Forward on SS Raster Shift
MediaTek Inc.
3GPP TSG-RAN WG4 AH-1801 Meeting R4-1801238
San Diego, CA, USA, January 22nd – 26th, 2018

## Slide 2: Background (1)
NR SS raster definition has been agreed in RAN4 #85 meeting and developed into the first revision of UE RF technical specifications.
To support LTE re-farmed bands with 100kHz channel raster, the SS raster entry has been formulated as,
  SS Entry = N*900kHz + M*5kHz, M = [-1:1]
The +/- 5kHz shift alongside N*900kHz is to assure the SS raster and channel raster frequency difference is a multiple of 15 kHz.
In this meeting, concern over existing SS raster entry formula with +/- 5kHz shift which could not support 30kHz SCS was raised [1-2].
  Proposal is to change +/- 5kHz shift to +/- 10kHz shift

## Slide 3: Background (2)
A separate concern was also raised in this meeting that the +/- 5kHz or +/- 10kHz shift could not be differentiated from other potential frequency shift sources during UE initial cell search, such as reference clock inaccuracy or Doppler shift [2-3].
One solution to mitigate the frequency shift ambiguity issue is to introduce an additional signaling in MIB or RMSI. However, this would incur the downside of signaling overhead.
Another solution is to use a wider frequency shift than 10 kHz to avoid the measured frequency offset uncertainty and potential signaling overhead as proposed in [2-3]. This solution may or may not require 3 sequential scanning at each 900kHz step and incur longer search time which needs to be studied.

## Slide 4: Background (3)
To support 15kHz or 30kHz SCS for 100kHz channel raster, in addition to +/- 10kHz shift as proposed in [1-2], the following frequency shifts (+/- in kHz) are also mathematically feasible.
20 | 110 | 200
40 | 130 | 220
50 | 140 | 230
70 | 160 | 250
80 | 170 | 260
100 | 190 | 280

## Slide 5: Way Forward
Companies are encouraged to study and compare the “pros” and “cons” of the following solutions:
  +/- 5kHz or +/- 10kHz shift with RMSI signaling [2]
  Wider frequency shift with 3 sequential raster scans at each 900kHz step and no RMSI signaling [2]
  Feasibility of possible frequency shift which allows single raster scan at each 900kHz step and no RMSI signaling [3]
Based on the above analysis, RAN4 to conclude the SS raster offset value in RAN4 #86 meeting.

## Slide 6: References
[1] R4-1800274, “Channel and sync raster alignment for 30 kHz SCS”, Ericsson, 3GPP TSG-RAN WG4 AH-1801 Meeting, January 22nd – 26th, 2018
[2] R4-1800481, “Further discussion on some issues of synchronization raster”, Huawei, HiSilicon, 3GPP TSG-RAN WG4 AH-1801 Meeting, January 22nd – 26th, 2018
[3] R4-1800299, “Reconsideration of NR sync raster for 100kHz channel raster”, MediaTek Inc., 3GPP TSG-RAN WG4 AH-1801 Meeting, January 22nd – 26th, 2018