## Slide 1: WF on performance testing for FR2
Keysight Technologies, [Intel], [Qualcomm], [Rohde & Schwarz], [Anritsu],
3GPP TSG-RAN WG4 NR Adhoc 1801 R4-1801265
San Diego, USA, January 22 – 26, 2018
Agenda item: 4.7.6
Document for: Approval

## Slide 2: Proposals
Proposal 1. Adopt “pure baseband” testing methodology for demodulation performance testing in FR2.
  Assumes max rank 2 with cross polarized transmission
  Rank 2 spatial MIMO would not be included
  As a starting point an isotropic UE antenna pattern is assumed
Proposal 2. Methodology for RRM testing in FR2 is further discussed during the SI.

## Slide 3: UE reporting requirements for baseband testing
In order to set up a two stream radiated connection to the DUT which does not include the antenna pattern it is necessary to use a cross-polarized point source transmission an then invert the channel matrix to enable independent control of the signals reaching each baseband receiver
To do this requires that the UE supports power measurement reporting per receiver port in a similar way to the RSAP measurement defined I 36.978 for LTE (but not based on CRS)
The relative phase between receivers is not required to calibrate the basic connection
Relative phase is required to enable UE antenna pattern measurement
  UE antenna pattern measurement is not required for isotropic antenna pattern emulation