## Slide 1: WF on FR2 Rx spurious emissions
NTT DOCOMO, INC.
3GPP TSG-RAN Working Group 4 (Radio) meeting AH-1801 R4-1801281
San Diego, USA, 22nd – 26th January, 2018
Agenda Item: 4.4.3.5.2 OTA receiver spurious emissions [NR_newRAT]

## Slide 2: Background
Following contributions have been discussed in RAN4 #85 and AH-1801:
  [1] R4-1713064, Discussion on OTA receiver spurious emission for FR2 NR BS, NTT DOCOMO, INC.
  [2] R4-1714433, TP to TS 38.104: OTA Rx spurious emissions for BS type O 2 (10.7.3), Huawei
  [3] R4-1800756, Discussion on FR2 Rx emissions, Huawei
  [4] R4-1800757, Draft CR to TS 38.104 - FR2 Rx emissions (10.7.3), Huawei
Following table for FR2 was agreed in RAN4 #85 [2]. However, some companies have concerns that the limits are lower than transceiver TDD OFF power limits.
Frequency range | Limit | Measurement bandwidth | Note
30MHz – 1 GHz | -57 dBm | 100 kHz | Note 1
1 GHz – 2nd harmonic of the upper frequency edge of the UL operating band | -47 dBm | 1 MHz | Note 1, Note 2
NOTE 1: Bandwidth as in ITU-R SM.329 [3], s4.1 NOTE 2: Upper frequency as in ITU-R SM.329 [3], s2.5 table 1. NOTE 3: The frequency range between 2.5 * BWChannel below the first carrier frequency and 2.5 * BWChannel above the last carrier frequency transmitted by the BS, where BWChannel is the channel bandwidth according to subclause 5.3, may be excluded from the requirement. However, frequencies that are more than ΔfOBUE below the lowest frequency of the BS transmitter operating band or more than ΔfOBUE above the highest frequency of the BS transmitter operating band shall not be excluded from the requirement. |  |  | 
Table 10.7.3-1: Radiated Rx spurious emission limits for BS type 2-O

## Slide 3: WF on OTA receiver spurious emissions for FR2
Following options can be considered for receiver spurious emissions limits.
  Option 1: Use Tx spurious emissions limits (same approach as FDD)
  Option 2: Use Tx OFF power limits
  Option 3: Use Rx spurious emissions limits (keep as E-UTRA)
  Other options are not precluded