## Slide 1
3GPP TSG-RAN WG4 Meeting AH-1801 R4-1801004 San Diego, US, 22 - 26 Jan, 2018
Agenda item: 4.2.1
Document for: Approval
WF on mixed numerology for CA
Huawei, HiSilicon,[ ]

## Slide 2: Background
RAN #78 agreement:
  For NR-NR CA, finalization of the work to enable up to 2 different numerologies within the same PUCCH group (PUCCH sent on the CC with smaller SCS) in RAN1 in Q1, and in RAN4 (Core) for Q2, for the December drop.
RAN4 agreement copied from chairman notes:
  Same numerology for intra-band NR CA including both continuous and non-continuous is mandatory support for Rel15.
Reference:
R4-1800421 on mixed numerology for CA, Huawei, HiSilicon
R4-1800516 Some clarifications for wideband operation of NR UE, LG

## Slide 3: UE Capability(1)
Intra-band CA:
  Option 1: Introduce mixed numerology as UE capability in Rel15
  Option 2: Introduce mixed numerology as UE capability in Rel16
  Option 3: it is not supported on mixed numerology in Rel15 for intra-band CA
Inter-band CA:
  same numerology are mandated to support, mixed numerology is introduced as capability
    UE shall support 2 numerologies with FR1+FR1 ,FR1+FR2, the number of CCs FFS.
Wideband operation with contiguous UE CCs: reuse intra-band contiguous CA case

## Slide 4: UE Capability(2)
Signalling:
  Option 1: Signaling of SCS per CC in BPC/BPC entry(baseband processing capabilities)
  Option 2: Signaling of SCS per BC
  Option 3: Signaling regardless of band combination: report UE capability on mixed numerology for CA per UE