## Slide 1: Way forward on RRC re-establishment and release with redirection
Huawei, HiSilicon, …
3GPP TSG-RAN WG4 Meeting #85 San Diego, USA, 22nd – 26th January 2018
Agenda Item: 4.6.10
R4-1801297

## Slide 2: RRC release with redirection
RAN2 has agreed to specify the procedure for RRC release with redirection for NR SA.
NR RRC release with redirection can be different with LTE.
Proposal for the requirement for NR SA RRC release with redirection to E-UTRA,
  [Tconnection_release_redirect_E-UTRA = TRRC_procedure_delay + Tidentify-E-UTRA + TSI-E-UTRA + TRA ]
    TRRC_procedure_delay shall be less than [TBD] ms.
    Tidentify-E-UTRA shall be less than [TBD] ms.
    TSI-E-UTRA is the time required for acquiring all the relevant system information of the target E-UTRA cell.
    TRA is the delay caused due to the random access procedure.
The requirements are for both E-UTRA TDD and FDD
RAN4 closely follows the progress of NR RRC release with redirection in RAN2.

## Slide 3: RRC re-establishment
NR RRC re-establishment can be different with LTE RRC re-establishment.
Proposal for the requirement for NR RRC connection re-establishment,
  [TUE-re-establish_delay = [TBD] ms + Nfreq* Tsearch + TSI + TPRACH ]
    Nfreq is the total number of frequency layers to be monitored for RRC re-establishment in NR SA opertaions.
    For Tsi, UE doesn’t need to read system information in some cases where this factor equals to 0.
    For Tprach, the minimum value is TBD.
    For the constant value of [TBD] ms, companies are encouraged to provide the value with rationale.
RAN4 closely follows the progress of NR RRC re-establishment in RAN2.