## Slide 1: 3GPP TSG-RAN WG4 Meeting AH#1801 San Diego, USA, 22 -26 January 2018
CATT, Nokia and Nokia Shanghai Bell
WF on MTTD and MRTD requirements for synchronous EN-DC and NR CA
R4-1801300

## Slide 2: Background (1/2)
Following contributions in RAN4 RRM session discuss the MTTD and MRTD requirements for synchronous EN-DC and NR CA:
  R4-1800514, Discussion for synchronous EN-DC, LG Electronics
  R4-1800052, Further discussion on MTTD and MRTD for EN-DC, CATT
  R4-1800515, Discussion on MRTD and MTTD for synchronous EN-DC, LG Electronics
  R4-1800597, Further discussions on synchronous and asynchronous Dual connectivity in Rel-15 LTE-NR combinations, Ericsson
  R4-1800145, Discussion on MRTD and MTTD for synchronous DC in Rel-15 LTE-NR combinations, Intel
  R4-1800145, Discussion on MRTD requirements for NR CA, Intel

## Slide 3: Background (2/2)
Factors involved for calculating MTTD:
  Factor 1: Propagation delay difference
  Factor 2: Initial transmission timing error
  Factor 3: Uncertainty of the reception time in the UE downlink
  Factor 4: Cell phase synchronization error or timing alignment error (TAE)
Factors involved for calculating MRTD
  Factor 1: Propagation delay difference
  Factor 2: Cell phase synchronization error or timing alignment error (TAE)

## Slide 4: Inter-band synchronous EN-DC
MTTD and MRTD
For higher order SCS, MTTD and MRTD shall be determined by taking the following aspects into account:
  All supported network deployment scenarios;
  Power control related issues;
  Other aspect is not precluded.
Sub-carrier spacing in LTE PCell (kHz) | DL Sub-carrier spacing in NR PSCell (kHz) | MTTD (µs) | MRTD (µs)
15 | 15 | 35.21 | 33
15 | 30 | [TBD] | [TBD]
15 | 60 | [TBD] | [TBD]
15 | 120 | [TBD] | [TBD]

## Slide 5: Intra-band synchronous EN-DC
Only consider collocation scenario for intra-band EN-DC in Rel-15 agreed in R4-1711964
Intra-band EN-DC
  MRTD requirement will be defined as [3]µs

## Slide 6: NR CA (1/3)
Inter-band CA
  For FR1 when all carriers have 15 kHz the MRTD is 33 µs.
  For FR1 with other combinations of SCS the MRTD is [TBD].
  For FR2 with same or different SCS MRTD is [TBD]
  For inter-band NR carrier aggregation between FR1 and FR2, the maximum receive timing difference is [TBD] µs.
  For DL CCs with different order SCS, MTTD and MRTD shall be determined by taking the following aspects into account:
    All supported network deployment scenarios;
    Power control related issues;
    Other aspect is not precluded.
  The table structure for MRTD requirements needs further consideration.

## Slide 7: NR CA (2/3)
Intra-band non-contiguous CA
  For FR1 when all carriers have 15 kHz the MRTD is 33 µs.
  For FR1 with other combinations of SCS the MRTD is [TBD].
  For FR2 with same or different SCS MRTD is [TBD]
  For inter-band NR carrier aggregation between FR1 and FR2, the maximum receive timing difference is [TBD] µs.
  For DL CCs with different order SCS, MTTD and MRTD shall be determined by taking the following aspects into account:
    All supported network deployment scenarios;
    Power control related issues;
    Other aspect is not precluded.
  The table structure for MRTD requirements needs further consideration.

## Slide 8: NR CA (3/3)
Intra-band contiguous CA
  No MRTD requirement will be defined.
  TAE for intra-band contiguous CA is specified in table 6.5.3.2-1 in TS.38.104, which is within CP.