## Slide 1: Way forward on Scell addition and activation delay
Intel, [], …
3GPP TSG-RAN WG4 Meeting AH-1801 San Diego, US, 22-26 January 2018
R4-1801303

## Slide 2: SCell activation delay
Background: it was agreed in RAN4#85 that “Upon receiving SCG SCell activation command in slot n, the UE shall be capable to transmit valid CSI report and apply actions related to the activation command for the SCell being activated no later than in slot n+ [THARQ + Tactivation_time + TCSI_Reporting ] ”
Tactivation_time is consisted of
  RF warm up excluding AGC settling: TBD and independent of SCS
  AGC settling: N1 SMTC periods for known and N2 SMTC periods for unknown cells
  PSS/SSS and SSB index acquiring:
    X1 SMTC periods for known cell
    X2 SMTC period for unknown cell
    X1 and X2 will be decided by RAN4#86
Side condition: SINR ≥ -3dB
Activation time for activation of multiple SCells; No. of SCells is FFS

## Slide 3: PScell addition delay
Background: it was agreed in RAN4#85 that “Upon receiving NR PSCell addition in subframe n, the UE shall be capable to transmit PRACH preamble towards NR PSCell no later than in subframe n + Tconfig PSCell:
Tconfig_PSCell = TRRC_delay + Tactivation_time + TSFN_acquisition + TPCell_ DU + TPSCell_ DU
Tactivation_time should be the same as defined in SCell activation delay

## Slide 4: Known PScell condition
Reuse the condition of known NR PSCell/SCell definition from LTE for FR1.
Define the condition of known NR PSCell/Scell for FR2.

## Slide 5: Tactivation_time Improvement
RAN4 to study the impact of potential additional signals (Aperiodic TRS, others not precluded) on T_activation