## Slide 1: Way Forward on the Number of Cells and Beams for SSB-Based Measurements
Ericsson, NTT DoCoMo, Nokia, Nokia Shanghai Bell, …
3GPP TSG-RAN WG4 Meeting AH-1801 R4-1801306
San Diego, USA, 22 - 26 January, 2018
Agenda Item: 4.6.2.2

## Slide 2: Background
In LTE, the UE is required to be able to measure and monitor the performance of:
  8 intra-frequency cells for each intra-frequency layer
  4 inter-frequency cells for each inter-frequency layer, up to 3 inter-frequency layers or 8 inter-frequency layers (with increased carrier monitoring)
In NR, UE is required to simultaneously monitor based on SSB at least [R4-1709909]:
  Below 6 GHz
    [8] intra-frequency cells
    [4] inter-frequency cells per frequency layer
The measurement capability shall be defined per reference signal type [R4-1709909]:
  Option 1: define capability on number of cells per frequency layer and number of beams per cell
  Option 2: define capability on number of beams per frequency layer
  Option 3: define capability on number of cells per frequency layer and number of beams per frequency layer
Agreements from R4-1713942
  Option 3a: define requirements on minimum number of cells per frequency layer UE should monitor and minimum number of SSBs with different SSB index and/or different PCI per frequency layer UE should monitor with at least 1 SSB per cell
    All aforementioned requirements should be satisfied during the same measurement period
From TS 38.133 1.0.0:
  For each intra-frequency layer the UE shall be capable of monitoring at least TBD cells.
  For each intra-frequency layer, during each layer 1 measurement period, the UE shall be capable of monitoring at least TBD SSB with different SSB index and/or PCI and the UE shall be capable of monitoring at least one SSB per cell.

## Slide 3: FR1
Number of cells
  8 intra-frequency cells
  4 inter-frequency cells per frequency layer
Number of beams
  [20] beams per intra-frequency, and
    On the serving cells, the UE shall be able to measure on at least N beams, where N is the number of configured RLM-RS resources for this cell
  [10] beams per inter-frequency

## Slide 4: FR2
Number of cells
  8 intra-frequency cells
  4 inter-frequency cells per frequency layer
Number of beams
  [24] beams per intra-frequency, and
    On the serving cell, the UE shall be able to measure on at least N beams, where N is the number of configured RLM-RS resources for this cell
  [12] beams per inter-frequency

## Slide 5
Annex: Summary of Companies’ Proposals
Company | FR1 |  |  |  | FR2 |  |  |  | Reference
 | Intra-frequency |  | Inter-frequency |  | Intra-frequency |  | Inter-frequency |  | 
 | # cells | # SSBs | # cells | # SSBs | # cells | # SSBs | # cells | # SSBs | 
Intel | 8 | 8 | 4 | 4 | 8 | 16 | 4 | 8 | R4-1800130
NTT DoCoMo | 8 | 32 | 4 | 16 | 8 | 32 | 4 | 16 | R4-1800563
ZTE | 8 | 24, 32 | 4 | 16 | 4 | ? | 4 | 24, 32 | R4-1800554
Huawei | 8 | 12, 14 | 4 | 8 | 4 | 16 | 3 | 12 | R4-1713406
Samsung | 8 | 12 | 4 | 8 | 4 | 16 | 2 | 8 | R4-1800199
Ericsson | 8 | 16 | 4 | 8 | 8 | 32 | 4 | 16 | R4-1800188
Qualcomm |  |  |  |  | 3,4 | 8,12 |  |  | R4-1800979
Nokia | 8 | 16 | 4 | 8 | 8 | >1 per cell | 4 | >1 per cell | R4-1800376
MediaTek | 8 | 8 | 4 | 4 | 8 | 16 | 4 | 12 | R4-1800106
CATT | 8 | 16 | 4 | 8 | 8 | 16 | 4 | 8 | R4-1712592