## Slide 1
3GPP TSG-RAN WG4 Meeting AH-1801 R4-1801323
San Diego, US, 22 - 26 Jan, 2018
Agenda item: 4.2.1.3
Document for: Approval
WF on
BWP switching
Huawei, HiSilicon,[ ]

## Slide 2: Background (1)
R1-1721712 LS on RAN1 agreement on bandwidth part transition time sent to RAN4
  RAN1 agreement
    The value range of the transition time(s) of active BWP switching are up to RAN4
    it’s also up to RAN4 to decide whether the transition time(s) of active BWP switching is reported to the network as dedicated UE capability or not.
  RAN1 would like to kindly ask RAN4 to take the above agreements into account.

## Slide 3: Background (2)
R4-1702029 provides values for RF transition times
  For intra-band operation, at least for sub6, the transition time can be up to 20 µs if the center frequency is the same before and after the bandwidth adaptation, regardless other conditions listed in the LS
  For intra-band operation, at least for sub6, the transition time is 50~200 µs if the center frequency is different before and after the bandwidth adaptation, regardless other conditions listed in the LS
  For inter-band operation, at least for sub6, the transition time can be up to 900 µs, regardless the conditions listed in the LS. RAN1 should note that this time does not include AGC settling time which is covered in baseband aspects.
  The values above 6 GHz, the values are FFS

## Slide 4: Proposed Working agreement
Changes in active BWP can occur from signaling in DCI and timer expiry
For intraband bandwidth part switching, there are 4 scenarios which involve possible changes in BWP configuration
  The reconfiguration involves changing the center frequency of the BWP without changing its BW. The reconfiguration may or may not involve changing the numerology.
  The reconfiguration involves changing the BW of the BWP without changing its center frequency. The reconfiguration may or may not involve changing the numerology.
  The reconfiguration involves changing both the BW and the center frequency of the BWP. The reconfiguration may or may not involve changing the numerology.
  The reconfiguration involves changing only the numerology, where the center frequency and BW of the BWP remain unchanged.

## Slide 5: Proposed Working agreements
In order to perform BWP switching, UE implementations may need switching time switching gapinterruptionsgaps for baseband processing, for retuning the local oscillator, for reconfiguring the RF chain for more or less bandwidth, for reconfiguring the RF chain for different numerologies, or for a combination of these operations.
The BWP switching delay parameters, includes both RF transition time and the BB processing time during BWP switching operation.
It is assumed that the change of BWP active configuration is confined within the UE CC. There may or may not be a change in numerology
It is assumed that during the BWP switching procedure the UE Tx will not transmit, and the UE Rx will not receive.
The UE may need interruption during the BWP switch operation. The interruption duration is FFS.
The BWP switching time is applicable to all UEs.

## Slide 6: Open issues
Definition of start of BWP switching operation on DL when BWP switch command received via DCI
  Option 1> The new BWP configuration becomes active at the slot boundary
  Option 1a> The BWP switching operation starts at the slot boundary after BWP reconfig command (via DCI ) is received
  Option 1b> The BWP switching operation starts is at the first slot boundary where UE has not grants after BWP switch command is received
  Option 2> After UE receives the DCI (last symbol containing DCI)
  Other options are not precluded
BWP switch time start based on time expiration is FFS
Definition of end of BWP switching operation
  Option 1> When the UE is capable of monitoring PDCCH with the new BWP numerology
  Option 2> immediately after the delay switch time
  Other options are not precluded
Values for FR2 as FFS because companies need time to obtain values
  Switching time such that the delay is not shorter than for FR1
Values for FR1 baseband processing times vary and companies need time to obtain values
Values for FR1 RF transition times should be updated based on the specified scenario listed in slide #4
Values for the RRM delays are FFS

## Slide 7: References
R4-1800117, “On BWP switching delay”, Intel
R4-1800118, “LS on RAN4 agreement on BWP switching delay”, Intel
R4-1800419, “On BWP switching time”, Huawei, HiSilicon
R4-1800420, “[draft] Reply LS on bandwidth part transition time”, Huawei, HiSilicon
R4-1800742, “On BWP switching delay”, Nokia, Nokia Shanghai Bell
R4-1702029, “Reply LS on UE RF Bandwidth Adaptation in NR”
R4-1800107, “Discussion on BWP transition time”, MediaTek