## Slide 1: Updated way forward on measurement gap timing offset based on R4-1800564
NTT DOCOMO
3GPP TSG-RAN WG4 Meeting AH-1801
San Diego, US, January 22nd - January 26th, 2018
R4-1801330
Document for: Approval
Agenda item: 4.6.4

## Slide 2: Background
RAN2 agreements at NR-AH 1801
RAN4 previous conclusion in R4-1711940
Agreements 1 For gap pattern configured by MN, UE performs gap calculation based on the SFN and subframe of PCell. 2 For gap pattern configured by SN, UE performs gap calculation based on the SFN and subframe of PSCell. 3 The configuration step of gapoffset in 36.331 is 1ms. FFS: Gapoffset in 38.331. To be checked with RAN4.
Measurement Gap offset should be configurable with granularity based on the maximum slot length of all the UE serving cells which have configured the gap.

## Slide 3: Background
RAN4 discussion at RAN4 NR-AH1801 meeting
  Based on R4-1800564
    In order to align effective measurement duration within MG with SMTC window timing, MG timing needs to have 0.5 or 0.25 ms advance from SMTC timing
    Since SMTC window timing offset has fixed 1ms granularity, applying 0.5ms or 0.25ms timing advance based on 1ms MG timing offset granularity is sufficient and finer granularity of MG timing offset would not be necessary
5 ms SMTC window timing
6 ms MG timing
Effective measurement duration (excluding RF retuning time)
Inter-freq carrier
0.5 ms timing advance
Example #1
Example #2
3 ms SMTC window timing
3.5 ms MG timing
Possible MG timings
Possible SMTC timings

## Slide 4: Background
RAN4 discussion at RAN4 NR-AH1801 meeting
  Potential solution based on R4-1800564
    UE and NW need to have exact same understanding on MG timing for scheduling purpose
    In some cases, MG timing advance is not necessary
      E.g., measurement on asynchronous NR carrier with 5 ms SSB periodicity
    Therefore, 1 bit indication signaling for MG timing advance (i.e., enabling/disabling) is proposed in R4-1800564
  Impact on LTE operation
    Some companies believe that the misalignment issue needs to be solved even when the UE has LTE serving cell for EN-DC operation
      If 0.5ms timing advance is applied, additional 1 subframe interruption on LTE serving cell(s) would happen
    Some other companies prefer to avoid/minimize the impact on UE behavior in LTE serving cell(s)

## Slide 5: Updated proposal
The measurement gap timing offset granularity is fixed to 1ms for all the cases.
  1 bit indication to enable/disable X ms timing advance to the configured measurement gap timing is supported.
    For per-UE-gap or per-FR-gap for FR1, X = 0.5
    For per-FR-gap for FR2, X = 0.25
    Detailed signaling design is up to RAN2
  UE is not expected to transmit PUCCH/PUSCH or receive PDCCH/PDSCH on serving cell(s) in slot(s) partially overlapping with MG as well as in slot(s) fully overlapping with MG
FFS: applicability of 0.5ms timing advance to MG when the MG affects LTE serving cell(s)