## Slide 1: Way forward on collision between paging occasion and SSB
Ericsson, Mediatek
3GPP TSG-RAN WG4 Meeting # AH1807
Montreal, Canada, July 02-06, 2018
Agenda: 5.2.5
R4-1809328

## Slide 2: Background
The network can configure the paging occasions (PO) wrt SSB of the serving cell in TDM manner or wrt SSB in FDM manner in RRC idle and RRC inactive states.
The PO configuration in TDM or FDM wrt SSB location may impact RRM measurement requirements in RRC idle and RRC inactive states and/or paging reception.
RAN2 has introduced a different definition of PO in 38.304 to that in 36.304.
  A PO is a set of PDCCH monitoring occasions and can consist of multiple time slots (e.g. subframe or OFDM symbol) where paging DCI can be sent.
  In multi-beam operations, the length of one PO is one period of beam sweeping and the UE can assume that the same paging message is repeated in all beams of the sweeping pattern and thus the selection of the beam(s) for the reception of the paging message is up to UE implementation.

## Slide 3: Way Forward
RAN4 to study the impact of restricting UE to not drop any paging due to SSB-based measurements regardless of whether paging occasion (PO) is TDM or FDM wrt the SSB location.
The RRM measurement requirements in RRC idle/inactive states may be impacted due to paging reception depending on at least the following parameters:
  DRX cycle length
  SMTC period
The RRM measurement requirements in RRC idle/inactive states may be impacted under the following scenario:
  When PO is FDM wrt SSB in FR2
  When PO is TDM wrt SSB in FR1
  When PO is TDM wrt SSB in FR2
Investigate until the next meeting (RAN4#88) how to address collisions, e.g.:
  Maximum DRX cycle length up to which the measurement times in RRC idle/inactive states need to be extended by certain scaling factor (X1, X2, X3)
  The value of the scaling factor, X1 for serving cell measurements and Nserv, X2 for intra-frequency measurements, X3 for inter-frequency measurements.
    Note: It is FFS whether values of X1, X2 and X3 are different or the same.
  SMTC period threshold above which the measurement times in RRC idle/inactive states need to be extended.