## Slide 1: Way forward on the DL power allocation and SNR definition for UE RF and demodulation requirements
Ericsson, …
3GPP TSG-RAN WG4 Meeting AH1807
Montreal, Canada, 2 – 6 July, 2018
R4-1809332

## Slide 2: Background
In LTE, the downlink power allocation setting for the UE demodulation and CSI reporting requirements are set with σA (RA) and σB (RB), which is the ratio of physical channel EPRE to the common reference symbol EPRE. However, NR has no CRS and TS36.101 cannot use RA/RB for power allocation setting.

## Slide 3: Way forward on DL power allocation
RAN4 will specify the DL power allocation as follow:
  The downlink SSS transmit power is defined as the linear average over the power contributions (in [W]) of all resource elements that carry the SSS within the operating system bandwidth (cf. TS38.214 4.1).
  EPRE of PBCH DMRS, PDCCH DMRS, PDSCH DMRS, OCNG DMRS, PSS, and NZP-CSI-RS are set relative to SSS EPRE
  EPRE of physical channels (PBCH, PDCCH, PDSCH, OCNG) are set relative to the EPRE of associated DMRS (e.g., PDSCH to PDSCH DMRS)
  EPRE of PTRS is set relative to the associated PDSCH
RAN4 is define the OCNG relative power level of the i-th virtual UE is defined as:
  γi = (EPRE ratio of PDSCHi to PDSCHi DMRS) / (EPRE ratio of OCNG to OCNG DMRS)
EPRE: Energy per Resource Element

## Slide 4: Example of DL power allocation (for information)
Parameter | Unit | Value
SSS transmit power | W | Test specific
EPRE ratio of PSS to SSS | dB | 0
EPRE ratio of PBCH DMRS to SSS | dB | 0
EPRE ratio of PBCH to PBCH DMRS | dB | 0
EPRE ratio of PDCCH DMRS to SSS | dB | 0
EPRE ratio of PDCCH to PDCCH DMRS | dB | 0
EPRE ratio of PDSCH DMRS to SSS | dB | 0
EPRE ratio of PDSCH to PDSCH DMRS | dB | Test specific
EPRE ratio of CSI-RS to SSS | dB | 0
EPRE ratio of PTRS to PDSCH | dB | Test specific
EPRE ratio of OCNG DMRS to SSS | dB | 0
EPRE ratio of OCNG to OCNG DMRS (Note 1) | dB | 0
Note 1: Number of DMRS CDM groups without data for PDSCH DMRS configuration for OCNG is set to 1. |  | 

## Slide 5: Way forward on SNR definition
Option 1: based on physical channel
  For SSS
  For PDSCH
  For PDCCH
  For PBCH
Option 2: based on DMRS for each physical channel
  For SSS
  For PDSCH:
  For PDCCH:
  For PBCH: