## Slide 1: WF on simulation assumptions for NR UE PDCCH demodulation tests in Rel-15
Ericsson
3GPP TSG-RAN WG4 Meeting #AH201807 Montreal, Canada, 27 Nov - 1 Dec 2017
Agenda Item: 5.4.1.3
R4-1809349

## Slide 2: Agreed work plan
The work plan for UE performance WI was agreed in R4-1808029.
  Phase 0: Overall test scope, generic common test set-up and channel modelling, specification skeleton
  Phase 1: Completion 1st bullet of test cases (RAN4 July Ad-hoc, RAN4#88)
    Demod:
      PDSCH: Normal test cases with single carrier
      PDCCH
    CSI: CQI (static), PMI, RI test cases
  Phase 2: Completion 2nd bullet of test cases (RAN4#88bis, RAN4#89)
    Demod:
      PDSCH: SDR test, CA/DC/SUL test cases if any
      PBCH if any
    CSI: CQI (fading), L1-RSRP, CRI test cases if any

## Slide 3: Previous agreements
The following agreements were made on Tuesday AH session captured in agreed adhoc minutes R4-1809347.
Test metric
  SNR @ 1% Pm-dsg
Aggregation level
  at least {2, 4, 8} , FFS for{ 1,16}
Channel bandwidth with subcarrier spacing and CORSET bandwidth in terms of number of RBs
  15kHz +10MHz for FR1 FDD
    24, 48
  30kHz +40MHz for FR1 TDD
    [102]
  120kHz +100MHz for FR2
    [60]

## Slide 4: CORESET configuration
Time duration
  2 for FR1 FDD 10MHz
  1 for FR1 TDD 40MHz
  1 for FR2 100MHz
Interleaved and non-interleaved
  Non-interleaved for FR1 10MHz
  Interleaved for FR1 40MHz
  Interleaved for FR2 100MHz
  Note: Interleaver size (R) = 3; Interleaver nshift = 0 [For alignment]
Precoder granularity
  Same as REG Bundle size
    Non-interleaved:6
    Interleaved: 2

## Slide 5: MIMO antenna configuration
FR1
  1x2, 2x2, 1x4, 2x4
  FFS on the test condition on 4Rx tests.
FR2
  1x2, 2x2
For 2Tx random precoder should be specified in RAN4 spec in Annex as beam forming model
  The precoder model is proposed in slides 11 for simulation purpose, other models are not precluded
  FFS for SSB/TRS/PTRS configurations
Low correlation ULA

## Slide 6: DCI format
DCI format
  1-0, 1-1
Bit size (DCM proposal)
  For DCI format 1_0: 28 bits +
  For DCI format 1_1: Maximum number within the set of bit sizes when all of mandatory features in DCI format 1_1 are turned on.
  DCM will provide a concrete number as the bit size for 1_1 in this week

## Slide 7: TDD pattern for PDCCH
Reuse same TDD pattern from REFSENS tests
  Further check feasibility of the above TDD pattern for Pm_dsg testing

## Slide 8: Channel model
FR1
  TDL-A, 30ns, 10Hz
  TDL-C, 300ns, 100Hz
  Note: For simulation alignment use propagation models defined in 38.901
FR2
  Follow the conclusion from PDSCH

## Slide 9: Receiver type
MMSE-IRC based on no inter-cell interference is modeled in Rel-15.

## Slide 10: PDCCH test cases
Test No. | SCS(KHz) | Format | CORESET RB | Payload | CORESET time duration | AL | CCE-to-REG Mapping | REG bundle size | Propagation condition | Antenna configuration with 2Rx | Antenna configuration with 4Rx
1 | 15 | 1_0 | 24 | 39 | 2 | 2 | Non-interleaved | 6 | TDL-A, 30ns, 10Hz | 1x2 Low | 1x4 Low
2 | 15 | 1_0 | 24 | 39 | 2 | 4 | Non-interleaved | 6 | TDL-C, 300ns, 100Hz | 2x2 Low | 2x4 Low
3 | 15 | 1_1 | 24 | [51] | 2 | 2 | Non-interleaved | 6 | TDL-C, 300ns, 100Hz | 1x2 Low | 1x4 Low
4 | 15 | 1_1 | 48 | [51] | 2 | 4 | Non-interleaved | 6 | TDL-A, 30ns, 10Hz | 1x2 Low | 1x4 Low
5 | 15 | 1_1 | 48 | [51] | 2 | 8 | Non-interleaved | 6 | TDL-C, 300ns, 100Hz | 2x2 Low | 2x4 Low
6 | 30 | 1_0 | 102 | 41 | 1 | 2 | Interleaved | 2 | TDL-A, 30ns, 10Hz | 1x2 Low | 1x4 Low
7 | 30 | 1_1 | 102 | [53] | 1 | 4 | Interleaved | 2 | TDL-C, 300ns, 100Hz | 1x2 Low | 1x4 Low
8 | 30 | 1_1 | 102 | [53] | 1 | 8 | Interleaved | 2 | TDL-C, 300ns, 100Hz | 2x2 Low | 2x4 Low
9 | 120 | 1_0 | [60] | 41 | 1 | 2 | Interleaved | 2 | TBD | 1x2 Low | NA
10 | 120 | 1_1 | [60] | [53] | 1 | 4 | Interleaved | 2 | TBD | 1x2 Low | NA
11 | 120 | 1_1 | [60] | [53] | 1 | 8 | Interleaved | 2 | TBD | 2x2 Low | NA

## Slide 11: For simulation purpose
Random precoders as listed in the table can be considered for 2Tx tests, taken from L1 spec 38.214

## Slide 12: For information
For stabilizing testing purpose, interested companies are encouraged to perform study on channel realization and PDCCH BLER spread based on the current agreed simulation assumptions from previous slides.