## Slide 1: Way forward on PBCH demodulation requirements
Ericsson
3GPP TSG-RAN WG4 Meeting AH1807
Montreal, Canada, 2 – 6 July, 2018
R4-1809350

## Slide 2: Agreements
RAN4 introduces the PBCH demodulation requirements in Rel-15.
Test metric:
  SNR_PBCH@1% Pm-bch. Pm-bch is defined as 1-A/B, where A is the number of correctly decoded MIB PDUs and B is the number of transmitted MIB PDUs.
Interested companies are encouraged to provide the PBCH simulation results in RAN4#88.
  Companies can prioritize PDSCH, PDCCH, and CSI simulations.
Receiver assumption
  Baseline: Single-shot decoding

## Slide 3: Simulation assumption (Common setup)
Parameters | Unit | Values
Cell ID |  | 0
CP length |  | Normal
Number of SS/PBCH blocks within an SS burst set periodicity |  | 1
SS/PBCH block index |  | 0
SS burst periodicity | ms | 20
MIB size | bits | 24
PBCH payload size (including CRC=24bits and 8 bits of SS/PBCH location information) | bits | 56

## Slide 4: Simulation assumption (For alignment purpose)
Parameters | Test 1 | Test 2 | Test 3 | Test 4
Frequency range | FR1 | FR1 | FR2 | FR2
Channel BW | 10MHz | 40MHz | 100MHz | 100MHz
SS/PBCH SCS | 15kHz | 30kHz | 120kHz | 240kHz
SS Block pattern (Note 2) | Case A | Case B Case C | Case D | Case E
Antenna configuration | 1x2 | 1x2 | 1x2 | 1x2
Propagation channel (Note 1) | TDL-C RMS DS=300ns Doppler=100Hz | TDL-A RMS DS=30ns, Doppler=10Hz | FFS | FFS
Note 1: Use PDP specified in TS38.901
Note 2: Depending on the operating band. Refers to TS38.101-1 Table 5.4.3.3-1 for which band uses which pattern