## Slide 1: Summary of operators input on the TDD patterns for NR UE performance tests in Rel-15
Ericsson
3GPP TSG-RAN WG4 Meeting #AH201807 Montreal, Canada, 27 Nov - 1 Dec 2017
Agenda Item: 5.4.1.3
R4-1809351

## Slide 2: Agreed work plan
The work plan for UE performance WI was agreed in R4-1808029.
  Phase 0: Overall test scope, generic common test set-up and channel modelling, specification skeleton
  Phase 1: Completion 1st bullet of test cases (RAN4 July Ad-hoc, RAN4#88)
    Demod:
      PDSCH: Normal test cases with single carrier
      PDCCH
    CSI: CQI (static), PMI, RI test cases
  Phase 2: Completion 2nd bullet of test cases (RAN4#88bis, RAN4#89)
    Demod:
      PDSCH: SDR test, CA/DC/SUL test cases if any
      PBCH if any
    CSI: CQI (fading), L1-RSRP, CRI test cases if any

## Slide 3: Background
Different operators/countries/regions have different planning and considerations on TDD patterns for different frequency bands.
The TDD config for the test set-up is still open for UE performance tests except the FR1 15kHz was agreed as following with the purpose to align the LTE config#2
  FR1:
    15 kHz: DDDSU(aligned with LTE config#2 with 5ms periodicity)
      S = 12D+1Gp+1U
The purpose of UE performance tests should reflect the practical networks based on actual deployment from operators.
In this document summarizes the preference from different operators for different SCS and FR with represents present in this AH meeting.

## Slide 4: FR1
30kHz
Region | Operators | First prior | Second prior
Japan | DCM | 7D1S2U, S = 6D:4G:4U | SU, S=12D:2G
China | CMCC | DDDSUDDSUU, S1(D,GP,U)=[10, 4, 0], S2(D, GP, U) = [10,4,0] | DDSU, S (D, GP, U) = [10,4,0]
Europe | Orange | DDDSU, S=10D:2G:2U | 7D1S2U, S = TBD

## Slide 5: FR2
60kHz
120kHz
Region | Operators | First prior | Second prior
Japan | DCM | DDDSU, S=10D:2G:2U | DSUU, S=12D:2G
US | AT&T | DDSU, S=11D+3G | 
Region | Operators | First prior
US | AT&T | DDSU, S=11D+3G

## Slide 6: WF for TDD patterns for NR UE performance tests in Rel-15
The UE performance tests should be defined based on the operators actual deployment plan to reflect the practical network condition
The total number of tests for PDSCH alignment should be considered as manageable for first round alignment in Aug meeting.
The first prior from each region and each SCS has the same level of priority when it comes to test setup
  Similar test scope should be covered for each TDD pattern as first prior e.g. MIMO config, channel model with doppler, MCS, etc.
  First prior should be considered for Phase 1 and collected with alignment results in Aug meeting
The second prior test will be defined with UE performance tests after first prior test set is completed, pending on the completed date if it’s included in Rel-15.