## Slide 1
China Telecom, AT&T, NTT DOCOMO, CMCC, Orange, China Unicom, Vodafone
3GPP TSG-RAN WG4 Meeting AH-1807
Montreal, CA, 2 - 6 July, 2018
Agenda: 5.4.2.2
R4-1809368
Waveform for NR PUSCH demodulation requirements

## Slide 2: Background
In the last meeting, the waveform for PUSCH demodulation requirements were discussed, and several vendors proposed that:
  Test cases are only defined for CP-OFDM based PUSCH.
In the email discussion on RAN4 reflector, operators expressed their concern on excluding DFT-S-OFDM based PUSCH, and an compromised proposal was given by operators:
  Test cases are defined for CP-OFDM based PUSCH in Rel-15
  Test cases are defined for DFT-s-OFDM at least for low SNR region (FFS: other case)
The justifications from the operators can be summarized as:
  The support of DFT-S-OFDM waveform is very important from NR coverage perspective.
  As per the RAN1 conclusion, for NR UL, both CP-OFDM waveform and DFT-S-OFDM waveform are mandatory without capability signaling.
  DFT-S-OFDM related UE requirements have been defined in RAN4.
No consensus on waveform was reached.

## Slide 3: Proposal
Both CP-OFDM and DFT-S-OFDM waveforms should be considered in PUSCH requirements in Rel-15.
  For DFT-s-OFDM waveform:
    Test cases are defined for low SNR region with low MCS.
    Test parameters are to be discussed in the next meeting.