## Slide 1: 3GPP TSG-RAN WG4 Meeting #AH-1807 Montreal, Canada, 2th – 6th July, 2018
Huawei, Ericsson, Nokia, Nokia Shanghai Bell, ZTE, CATT
Way forward on General part of NR BS demodulation performance
R4-1809370

## Slide 2: General - 1
Define requirements only for a subset of the BS channel bandwidths in TS 38.104.
Applicability
  Apply the BS demodulation test cases according to BS declaration
  FFS if BS is required to pass tests for all declared SCS
  BS is only required to pass tests for one BW selected from BS declared BWs
    In principle, if the selected BW for testing is not in the subset with defined performance requirements, this BW will be tested based on the requirements of the nearest lower BW (i.e. reference BW) in the subset.
    In the test, the reference BW will be placed in the middle of the BW for PUSCH and PUCCH, FFS for PRACH
Duplex mode
  FR1: FDD, TDD and SUL
  FR2: TDD

## Slide 3: General - 2
SCS and Bandwidth
  Below bandwidth is agreed as the minimum set, additional test cases can be defined based on operators’ request.
  FFS: if RF decision on BW needs to be taken into account.
    15kHz: 10MHz, 20MHz
    30kHz: 20MHz, 40MHz, 100MHz
    60kHz(FR2): 100MHz
    120kHz: 100MHz, 200MHz
  Below is requested by operators as additional cases
    30kHz: 60MHz, 80MHz
    120kHz: 50MHz
TDD UL-DL configuration
  FR1: FFS which UL/DL configuration is used for the TDD tests
  FR2:
    Option 1: {DDDSU}, S = {D10, G2, U2}
    Option 2: {DDSU}, S={D11, G3}
    Option 3: {DDSU}, S={D8, G3, U3}
    Option 4: {DDDSDDDSUU}, S={D10,G2,U2}
    Other options not precluded
  FFS if requirement should be defined for one or multiple UL/DL configuration

## Slide 4: General - 3
PT-RS
  PTRS will be configured in FR2 test cases.
  FFS whether PN is modelled in the test cases.
  Companies are encouraged to input the studies on impact of PN.
Antenna configuration
  FR1 conducted: 2Rx, 4Rx, 8Rx.
  FFS solutions to conduct conformance testing for BS with >8 antenna connectors.
Applicability rule for CA, EN-DC, SUL
  NR CA: same applicability as in LTE
  EN-DC: FFS
  SUL: reuse FDD