## Slide 1: WF on MU of receiver directional requirements
Nokia, Nokia Shanghai Bell, Ericsson, Huawei, NTT DOCOMO, INC.
3GPP TSG-RAN WG4 Meeting AH-1807 LTE/NR perf
Montreal, Canada, 2th – 6th July 2018
Agenda Item: 4.2.1.1.3.1
R4-1809428

## Slide 2: Background
Contributions on MU for eAAS and NR FR1 OTA receiver directional requirements have been discussed in RAN4:
  [1] R4-1808654, “Necessity of PA for OTA Adjacent channel selectivity and narrowband blocking measurement for eAAS for FR1”, Ericsson.
  [2] R4-1808658, “Proposals on MU and TT for OTA receiver directional requirements”, Nokia, Nokia Shanghai Bell.
  [3] R4-1809184, “How to calculate MU for OTA RX directional requirements”, Huawei.

## Slide 3: Way forward on MU for eAAS and NR FR1 OTA receiver directional requirements
MU for dynamic range: Adopt conducted MU for OTA.
Conducted MU: Conducted MUs for wanted and interfering signals already include 95% confidence level, hence no need to multiply MU by 1.96 for summation.
Mismatch uncertainty: Use the EIS measurement uncertainty from the source ‘Impedance mismatch in the transmitting chain’ and ‘Standing wave between DUT and test range antenna’ recorded in TR 37.842 as the mismatch uncertainty for IAC and CATR, respectively, for the frequency range below 4.2 GHz for both conducted and OTA parts.
Need for PA: Do not include additional PA MU.
Companies are encouraged to input EIS MU for NR FR1 (4.2GHz < f ≦ 6GHz) in RAN4 meeting#88. If no further analysis on NR FR1 according to the agreed timeline, the same MU budget as eAAS (3GHz < f ≦ 4.2GHz) can be reused for NR FR1 (3GHz < f ≦ 6GHz).

## Slide 4: MU values for IAC based on way forward
 | Expanded uncertainty ue [dB] |  | 
 | f ≦ 3GHz | 3GHz < f ≦ 4.2GHz | 4.2GHz < f ≦ 6GHz
receiver dynamic range | 0.3 | 0.3 | TBD
adjacent channel selectivity, narrowband blocking, and in-channel selectivity | 1.7 | 2.0 | TBD
in-band blocking | 1.8 | 2.1 | TBD
receiver intermodulation | 2.0 | 2.5 | TBD

## Slide 5: MU values for CATR based on way forward
 | Expanded uncertainty ue [dB] |  | 
 | f ≦ 3GHz | 3GHz < f ≦ 4.2GHz | 4.2GHz < f ≦ 6GHz
receiver dynamic range | 0.3 | 0.3 | TBD
adjacent channel selectivity, narrowband blocking, and in-channel selectivity | 1.7 | 2.1 | TBD
in-band blocking | 1.9 | 2.2 | TBD
receiver intermodulation | 2.0 | 2.6 | TBD

## Slide 6: Final MU values based on way forward
 | Expanded uncertainty ue [dB] |  | 
 | f ≦ 3GHz | 3GHz < f ≦ 4.2GHz | 4.2GHz < f ≦ 6GHz
receiver dynamic range | 0.3 | 0.3 | TBD
adjacent channel selectivity, narrowband blocking, and in-channel selectivity | 1.7 | 2.1 | TBD
in-band blocking | 1.9 | 2.2 | TBD
receiver intermodulation | 2.0 | 2.6 | TBD