## Slide 1: WF on test cases for NR BS
ZTE,[...]
3GPP TSG RAN WG4 AH-1807 R4-1809466
Montreal, Canada, 2-6 July, 2018

## Slide 2: Background (1)
In RAN4#87, it was agreed that RF channels B (bottom), M (middle) and T (top) should be considered case by case for NR in the WF[1]
In RAN4#AH-1807, several contributions discussed the NR test cases:
  R4-1809153 On test cases for NR BS conformance tests, Nokia, Nokia Shanghai Bell
  R4-1808814 RF channel for NR BS RF conformance test, ZTE Corporation
  R4-1808815 TP for TR38.141-1: RF channel (section 4.9.1), ZTE Corporation
  [1] R4-1808318, WF on Test cases for NR BS conformance test, Huawei, Ericsson, Nokia,ZTE

## Slide 3: Way forward on NR test cases (1)
Down-selection of channel bandwidth case by case for single carrier cases
  Option 1: lowest and highest bandwidth supported and declared by BS vendor for both FR1 and FR2.
  Option 2: Other methods should not be precluded.
Down-selection of SCS for single carrier cases
  Option 1: Only the supported narrowest SCS should be selected
  Option 2: The supported narrowest SCS should be selected. For OBUE requirement, the highest supported SCS shall be considered when testing with widest supported CBW.
  Option 3: Narrowest CBW with supported narrowest SCS and widest CBW with supported highest SCS

## Slide 4: Way forward on NR test cases (2)
Down-selection of RF channels B/BRFBW(bottom), M/MRFBW (middle) and T /TRFBW (Top) :
  For transmitter spurious emission
    FR1 and FR2
      Option 1: B and T for single carrier; BRFBW, TRFBW for multi-carrier and/or CA
      Option 2: B, M, and T for single carrier; BRFBW, MRFBW, TRFBW, multi-carrier and/or CA
    FR2
      B and T for single carrier; BRFBW, TRFBW for multi-carrier and/or CA
  For transmitter intermodulation ,in-band general blocking and receiver intermodulation for both FR1 and FR2
    If the outermost edge of interfering signal is within operating bands, M for single carrier for both FR1 and FR2; MRFBW for multi-carrier and/or CA for both FR1 and FR2
    Otherwise, B and T for single carrier; BRFBW, TRFBW for multi-carrier and/or CA
  For narrow band blocking (only for FR1 and FR2?)
    Option 1: M for single carrier; MRFBW for multi-carrier and/or CA
    Option 2: B, M, and T for single carrier; BRFBW, MRFBW, TRFBW, multi-carrier and/or CA
  For other requirements
    Reuse the RF channel approach for the same requirements in E-UTRA for NR BS FR1 and FR2
For muti-band operation,the RF channel approach defined in E-UTRA shall be reused for the same requirements for NR BS FR1 and FR2