## Slide 1: WF on the test model
Huawei, …
3GPP TSG-RAN WG4 Meeting AH1807
Montreal, Canada, 2 – 6 July, 2018
R4-1809467

## Slide 2: References
[1] R4-1808320, “WF on test models for NR conformance test,” Nokia, Nokia Shanghai Bell, RAN4#87, May 21-25, 2018.
[2] R4-1808894, “Discussion on NR Test model”, ZTE, RAN4#AH-1807, July 2-6, 2018
[3] R4-1809115, “On synchronized LTE-NR general Test model parameters for TDD UL/DL configuration,” Ericsson, July 2-6, 2018
[4] R4-1809116, “Test Models for NR and Waveform Properties,” Ericsson, July 2-6, 2018
[5] R4-1809117, “On NR test model coverage for multiple numerologies and power boosting/deboosting,” Ericsson, July 2-6, 2018
[6] R4-1809150, “Parameters for NR test models,” Nokia, Nokia Shanghai Bell, July 2-6, 2018
[7] R4-1809151, “Further discussion on NR test models for BS conformance tests,” Nokia, Nokia Shanghai Bell, July 2-6, 2018
[8] R4-1809239, “Introducing a mixed numerology test model,” Huawei, July 2-6, 2018
[9] R4-1809240, “Channel parameters for TM design,” Huawei, July 2-6, 2018
[10] R4-1809241, “Efficient parameterization of test models,” Huawei, July 2-6, 2018
[11] R4-1809242, “Applicability of E-UTRA test models for NR,” Huawei, July 2-6, 2018

## Slide 3: Background
From RAN4#87 in Busan, WF [1] captured
Each of NR test model consist of following elements:
  Core requirements list for which given test model is used,
  Physical channel parameters of test model,
  Most of TMs include tables of specific parameters that are used for test models (eg. boosters PRBs, allocated PRBs etc. for both FDD and TDD).
Companies are encourage to further study if all TM that are used in E-UTRA test specification are needed for NR.
Companies are encourage to further study which aspects of the NR PHY design and channels parameters are needed for TM design.
For each TM specific list of parameters should be create. There may be different list of parameters for each frequency range.
Efficient way to introduce list of parameters for TM (eg. boosted PRBs and allocated PRBs for given test models) should be consider.
For NR TDD operation configuration of TDD gNB needs to be decided to define test models.
Companies are encouraged to further study the test for mixed numerologies and decide further if we need the mixed numerologies tests.

## Slide 4: E-UTRA Test models applicability to NR
E-UTRA Test model | Comments
E-TM1.1 | Most companies agree on this model (no DL RS accuracy)
E-TM1.2 | Investigate need for power boosting
E-TM2 | Several companies agree on this model
E-TM2a | Several companies agree on this model
E-TM3.1 | Several companies agree on this model
E-TM3.1a | Several companies agree on this model
E-TM3.2 | Investigate power boosting, test formulation
E-TM3.3 | Investigate power boosting, test formulation
WF: Intension to use same test models for FR1 and FR2 (with different parameters where necessary)

## Slide 5: Discussion on TDD Configuration
Option 1: “DSUUU DDDDD” with S slot=11D 1Gp 2U [3]
  Configuration aligns with multi-RAT (LTE)
Option 2: 4D/1U with D slot=12D 1Gp 1U and U slot=1D 1Gp 12U [7]
Option 3: proposes “DDDSU” with S slot=12D 1Gp 1U [9]
  Consistent with UE and BS demod configurations LTE configuration #2
WF
  Downselect from 3 options
    May need to evaluate impact for legacy and MSR testing
  TDD configuration should consider impact of MSR, NB-IoT and NR coexistence
    Frame alignment between different RATs should be considered
  Other options than 1 – 3 are not precluded.
  Alignment between different SCS should be considered

## Slide 6: Discussion on Power Boosting
Power boosting/deboosting present in E-TM1.2, E-TM3.2, E-TM3.3
  Ericsson [5] showed results showing boosting may not be necessary
  Nokia considering whether boosting is necessary
  Huawei expressed some concern about necessity of boosting for DPD
WF
  Companies encouraged to present results to evaluate necessaity of LTE-based boosting / deboosting in next meeting
    If boosting/de-boosting not necessity is not shown, simplification of test models is possible considered
    If boosting/de-boosting has impact upon RF requirements/performance, considerations of this parameter may be considered in the test model
    If boosting/deboosting necessary, consider parameterizations to identify sets of RBs (to simplify specification)

## Slide 7: Discussion on Mixed numerology
[8] proposes examining a mixed numerology test model for unwanted emission
[5] and [7] propose no mixed numerology test model
WF
  Companies are encouraged to bring analysis to justify a need for additional testing with mixed numerologies for unwanted emission or other RF requirements. evaluation a mixed numerology model to see if unwanted emission is observed
    If no unwanted emission observed, no need to introduce mixed numerology test model

## Slide 8: PDCCH layout
Option 1: [2],[9] propose PDCCH in spanning entire first symbol of slot
Option 2: [4] propose 6 RBs over first 2 symbols of slot, remainder symbol is PDSCH
WF
  Downselect between two options
    Consider EVM aspects and DM-RS
    Define DM-RS layout
  Agreement: Consider PDCCH, PDSCH only as channels for TM design. PBCH (the impact/need for SS for EVM requirement is to be analyzed)
  PDCCH and PDSCH lay out specifics should be considered (RSs to be considered and their densities), with the objective of the impact to the overall waveform on RF requirements
  Companies are encouraged to provide parameterized designs